## Slide 1: Example of traffic management solution (2): Variable Speed Limit
A research group of:
26th of July 2023
SMART Ankara Sustainable Urban Mobility Plan Contract No. NEAR/ANK/2021/EA-RP/0124
Francisco Rodero

## Slide 2: Agenda
Time | Title/activity
10:00-10:05 | Introduction to agenda
10:05-10:45 | Example of traffic management solution (1): traffic light optimization
10:45-11:20 | Example of traffic management solution (2): Variable Speed Limit (Online connection)
11.20-11:30 | Break
11:30-12:30 | ITS solutions for public transportation.
12:30-13:30 | Lunch
13:30-14:00 | ITS solutions for urban logistics
14:00-14:45 | Workshop (1): Traffic light optimizations for public transport. Study case of Ankara.
14:45-15:00 | Break
15:00-15:50 | Workshop (2): strategic ITS plan for Ankara.
15:50-16:00 | Questions and Closing Remarks
16:00 | End of the second day of TM4

## Slide 3: Example of traffic management solution (2): Variable Speed Limit
Introduction
Contextualization and description of the problem to solve
Construction and calibration of the model, definition of the scenarios and feasible corridors where system will be applied.
Task a: Microsimulation and definition of the variable speed limit system
Methodology and design of the algorithm used by the system and indicators gathered for each scenario
Task b: Algorithm and indicators
Results of the operation, indicators and economical impact.
Assessment of the corridor

## Slide 4
Introduction: Contextualization
Concentrations of several high-capacity roads (C-58, C-33 and C-17) in the accesses through the northern area of ​​Barcelona.
The proximity to several urban centers (Ciutat Meridiana, Torre Baró and Vallbona) promotes the generation of problems of congestion and both air and noise pollution, especially in the highlighted area, where up to 20 lanes are concentrated in parallel.
Resolution 134 / XII dated October 31st 2018 of the Parliament of Catalonia urges the Government of the Generalitat to implement, with the necessary previous studies, a variable speed system on these roads within the framework of the Infrastructure Master Plan in the Barcelona Metropolitan Region.
As a previous step to the implementation of a variable speed system, the Catalan Traffic Service, commissions CENIT for a study where one of the main objectives is the definition of an algorithm of the variable speed system based on traffic simulation that, taking into account the existing boundary conditions and constraints, controls the maximum speed while minimizes the environmental impact and eases the management of the traffic.

## Slide 5
Introduction: Contextualization

## Slide 6
Task a: Microsimulation and definition of the variable speed limit system

## Slide 7
Task a: Road network
Review of lane configuration and speeds
Starting point created from OpenStreetMap cartography

## Slide 8
Task a: Road network
Review of lane configuration and speeds
Starting point created from OpenStreetMap cartography

## Slide 9
Task a: Road network
Review off allowed turns for each junction or node
Starting point created from OpenStreetMap cartography

## Slide 10
Task a: Road network
In addition to the previous items, the model also includes:
Horizontal and vertical signaling (i.e., marks, give way/stop signs and traffic lights configuration in the urban side of the highways).
Definition of the fleet categories that can be found in the roads of Catalonia (2017): percentage for different fuel type and corresponding Euro standard.

## Slide 11
Task a: Scenario definition
Peak Hour Morning
05:00h-10:00h
Off-peak
10:00h-14:00h
Peak Hour Evening
14:00h-20:30h
Night Time
20:30-00:00h
4SMD7
7SMD2
9SMD2
10SMD7
12SMD2
14SMD2

## Slide 12
Task a: Demand of the model
1
Error filtering
Aggregation by type of day
2
3
Derived calculations
Turn percentages
Real Data Sets (RDS)
Demand objects in the simulator

## Slide 13
Task a: Tools for calibration
RDS
Real Data Sets created from traffic loops allow to check if simulated behavior matches reality.
In this model, one point for each segment has been selected and the comparison is made in terms of traffic flow and speed.
Area not simulated
The area being analyzed may be affected by parts of the road network that are not included in the model.
In the urban side, the traffic flow is controlled by the first traffic light accessing the 50km/h zone.
In the rest of ends of the network, maximum speed is dynamically regulated based on historical information from INRIX by means of Aimsun strategies.
Logic code | Date | Speed | average | reference
447400052 | 2019-03-13 17:15 | 86 | 71 | 80
447400052 | 2019-03-13 17:20 | 74 | 71 | 80
447400052 | 2019-03-13 17:25 | 79 | 71 | 80
447400052 | 2019-03-13 17:30 | 71 | 71 | 80

## Slide 14
Task a: Tools for calibration
Behaviour
Some configuration parameters that define the behaviour of the vehicles have been modified according to what has been observed in traffic cameras:
Reaction time
Car-following: Configuration of aggressiveness  distance between vehicles depends on speed (stop&go effect).
In some sections: values for cooperation and aggressiveness during lane changing and acceleration/deceleration rate.

## Slide 15
Task a: Tools for calibration

## Slide 16
Task a: Calibration results
Peak Hour Morning
05:00h-10:00h
VEHICLE COUNT
SPEED (km/h)
REAL
SIMULATION

## Slide 17
Off-peak
10:00h-14:00h
Task a: Calibration results
VEHICLE COUNT
SPEED (km/h)
REAL
SIMULATION

## Slide 18
Task a: Calibration results
Peak Hour Evening
14:00h-20:30h
VEHICLE COUNT
SPEED (km/h)
REAL
SIMULATION

## Slide 19
Night Time
20:30-00:00h
Task a: Calibration results
VEHICLE COUNT
SPEED (km/h)
REAL
SIMULATION

## Slide 20
Task a: Calibration results (Summary)
Vehicle speed
Vehicle count

## Slide 21
Task b: Algorithm and indicators

## Slide 22
Task b: Methodology
The objective of the VSL system is to spread the vehicles along the road to reduce the density in the hot spots. Reducing density avoids having traffic jams situation which drive to a reduction of speed and capacity. As shown in the picture on the left (flow vs density), from 30 vehicles/km per lane on, congestion appears, impacting over the capacity and creating queues upstream.
The System is based on the fundamental diagrams on traffic flow, to be more specific, taking into consideration the relation between speed and flow (picture on the right).
When the speed of a road section is reduced, flow is also reduced and therefore, limiting the entrance of vehicles downstream, avoiding the increase of density on them.

## Slide 23
Task b: Algorithm
The algorithm starts analyzing the nearest section to the city. If density here is over the optimal and the flow in the first upstream section is over the maximum allowed based on its capacity, then the maximum speed in the upstream section is reduced. This action will reduce the flow in the analyzed section, trying to avoid an increase of the density. It is important to remark that the objective is not to move the bottleneck from one section to the one upstream but to spread the density along the road.
On the other hand, if the flow is lower than the maximum allowed, the maximum speed of the first upstream section is increased (without overpassing the speed limits).
Then, it iterates with the same rules over the next upstream section until the end of the road network analyzed in the project.
The algorithm is executed every 5 minutes of simulation. Constraints avoid changes between consecutive sections greater than +20km/h (abrupt acceleration prevention = sustainable driving) or lower than -40km/h (abrupt deceleration prevention = safety).

## Slide 24
Task b : Indicators
Traffic performance
Emissions
Average queue
Travel time
Lane changes
Vehicle stops
Stop time
CO2
NOX
PM10
Noise
INDICATOR | DESCRIPTION
Queues are a direct consequence of not flowing traffic. And increase the stop & go effect
Not flowing traffic impacts on travel time, situation which is directly perceived by the drivers.
It represents how important is the interaction between vehicles. The bigger the interaction is, the closer the vehicles are. If vehicles are closer, speed is reduced.
It is a colorless, dense and unreactive gas, which is part of the layer of the atmosphere closest to the earth, it has a great impact on the so-called greenhouse effect
These are toxic gases, irritants and precursors of the formation of nitrate particles, which lead to the production of acids and high levels of PM2.5 in the environment
These particles are behind numerous respiratory illnesses, cardiovascular problems, and lung cancers. Exposure to these can reduce life expectancy by several months to two years.
Another aspect to consider is the level of noise generation, especially in the sections closest to inhabited areas. Therefore, another indicator considered will be the level of generation, not propagation, of the noise in the different scenarios.
The lower the number of stops is, the greater the traffic flow is. It has direct impact on the environment.
Defines the level of congestion. The more severe is the congestion the bigger the stop time will be.

## Slide 25
Assessment

## Slide 26
Assessment: Segmentation
1
2
3
4
5
Length | Lanes | Entrances | Exits
1500m | 3 (*) | 2 | 0
1600m | 3 | 0 | 1
1375m | 3 (**) | 1 | 1 (HOL)
1400m | 3 | Service lane
1125m | 3 | 0 | 0
(*) during 1150m there 4 and 5 lanes to support two consecutive entrances
(**) during 150m there are 4 lanes to support the entrance to the high-occupancy lane
4SMD7
7SMD2
9SMD2
10SMD7
12SMD2
6
14SMD2

## Slide 27
Assessment: Results
Peak Hour Morning
05:00h-10:00h
DENSITY (veh/km)
SPEED (km/h)
VARIABLE SPEED
CURRENT
1
2
5
4
3

## Slide 28
Assessment: Conclusions
Peak Hour Morning
05:00h-10:00h
No VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Average queue (veh) | 8,39 | 7,35 | 0,04 | 0,00 | 0,05 | 15,83
 | Lane changes | 2,00 | 2,92 | 1,75 | 1,61 | 3,05 | 11,34
 | Number of stops | 3,62 | 2,91 | 0,03 | 0,00 | 0,04 | 6,60
 | Stop time (s) | 25,74 | 26,49 | 0,16 | 0,00 | 0,19 | 52,58
 | Travel time (h) | 522,18 | 473,87 | 264,77 | 289,97 | 233,26 | 1784,05
Emissions | C02 (tn) | 14,69 | 12,66 | 5,52 | 6,08 | 6,31 | 45,25
 | N0X (Kg) | 46,98 | 46,45 | 31,39 | 35,02 | 33,56 | 193,40
 | PM (Kg) | 8,73 | 6,40 | 0,68 | 0,75 | 1,65 | 18,20
Noise (db) |  | 90,30 | 94,14 | 93,24 | 92,83 | 90,79 | 92,26
VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Cua mitjana(veh) | 2,82 | 0,47 | 0,04 | 0,00 | 0,03 | 3,36
 | Canvis de carril | 1,56 | 3,23 | 2,40 | 1,83 | 3,14 | 12,16
 | Parades per vehicle | 1,42 | 0,25 | 0,04 | 0,00 | 0,02 | 1,74
 | Temps de parada (s) | 8,74 | 1,64 | 0,17 | 0,00 | 0,14 | 10,69
 | Temps de viatge(h) | 368,98 | 427,16 | 378,55 | 349,81 | 243,67 | 1768,17
Emissions | C02 (tn) | 9,84 | 7,63 | 5,65 | 6,00 | 6,01 | 35,13
 | N0X (Kg) | 36,48 | 33,90 | 27,23 | 31,53 | 31,84 | 160,98
 | PM (Kg) | 4,84 | 2,52 | 1,18 | 0,78 | 1,46 | 10,78
Nouse (db) |  | 90,30 | 94,14 | 92,80 | 92,90 | 91,79 | 92,39
The VSL avoids reaching very high densities (>40veh/km) during the peak hour in sections close to the city. Thus, density in other sections increase as expected.
Indicators reveal that when reducing density in the initial sections, traffic improves (queue reduction, less stops and lower travel time). At the same time, there is an impact in the speed and travel time in upstream sections. However, the overall performance is better than without speed control.
Reducing stops and queues significantly reduces emissions in the initial sections while increases in upstream sections. However, the overall reduction is relevant as shown by the corresponding indicators.

## Slide 29
Assessment: Indicators
Peak Hour Morning
05:00h-10:00h
VARIABLE SPEED
CURRENT
Chart: Density (veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 30.4793 | 21.4854 | 10.6278 | 11.6326 | 7.4375 | 16.3325
Amb sistema VSL | 21.9015 | 19.6561 | 16.5336 | 14.5551 | 7.7239 | 16.0741
Chart: Speed (km/h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 46.4936 | 76.3693 | 98.2866 | 98.7194 | 96.7735 | 83.3285
Amb sistema VSL | 58.4837 | 65.3364 | 69.5378 | 82.0351 | 93.5558 | 73.7898
Chart: N0X (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 46.9795 | 46.4505 | 31.3937 | 35.0201 | 33.5585 | 193.4024
Amb sistema VSL | 36.477 | 33.9039 | 27.2308 | 31.5284 | 31.8402 | 160.9802
Chart: PM (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 8.7269 | 6.3981 | 0.67925 | 0.75037 | 1.6493 | 18.2039
Amb sistema VSL | 4.8413 | 2.5167 | 1.1799 | 0.77615 | 1.4645 | 10.7785
Chart: C02 (tn)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 14.6876 | 12.6557 | 5.5203 | 6.0792 | 6.3067 | 45.2495
Amb sistema VSL | 9.8356 | 7.6274 | 5.6483 | 6.0049 | 6.0146 | 35.1307
Chart: Average queue (veh)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 8.3935 | 7.3505 | 0.039222 | 0 | 0.046639 | 15.8298
Amb sistema VSL | 2.8179 | 0.46544 | 0.042792 | 0 | 0.033722 | 3.3599
Chart: Stops (#/veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 3.6221 | 2.9099 | 0.030728 | 0 | 0.035079 | 6.5978
Amb sistema VSL | 1.4206 | 0.25213 | 0.038374 | 0 | 0.024227 | 1.7353
Chart: Travel time (h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 522.1789 | 473.8722 | 264.7683 | 289.9733 | 233.2567 | 1784.0493
Amb sistema VSL | 368.9842 | 427.1587 | 378.5538 | 349.8073 | 243.6676 | 1768.1716

## Slide 30
Assessment: Results
DENSITY (veh/km)
SPEED (km/h)
VARIABLE SPEED
CURRENT
Off-peak
10:00h-14:00h
1
2
5
4
3

## Slide 31
Assessment: Conclusions
For this time interval, the algorithm only works during the first 15 minutes where sections “recover” their usual speed limit because of low traffic density.
After this short transition, the algorithm stops because it is not actually needed.
No VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Average queue (veh) | 0,06 | 0,00 | 0,10 | 0,00 | 0,06 | 0,23
 | Lane changes | 1,87 | 3,02 | 2,25 | 2,48 | 2,87 | 12,49
 | Number of stops | 0,04 | 0,00 | 0,02 | 0,00 | 0,03 | 0,09
 | Stop time (s) | 0,17 | 0,03 | 0,36 | 0,02 | 0,20 | 0,77
 | Travel time (h) | 251,51 | 260,79 | 233,70 | 267,17 | 231,00 | 1244,18
Emissions | C02 (tn) | 5,01 | 5,75 | 4,75 | 5,58 | 5,12 | 26,21
 | N0X (Kg) | 23,37 | 30,70 | 26,91 | 31,74 | 27,81 | 140,52
 | PM (Kg) | 1,55 | 1,14 | 0,52 | 0,58 | 0,86 | 4,65
Noise (db) |  | 89,01 | 93,87 | 93,40 | 93,28 | 92,31 | 92,37
VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Average queue (veh) | 0,09 | 0,00 | 0,10 | 0,00 | 0,07 | 0,25
 | Lane changes | 1,88 | 3,04 | 2,26 | 2,49 | 2,87 | 12,54
 | Number of stops | 0,05 | 0,00 | 0,02 | 0,00 | 0,03 | 0,10
 | Stop time (s) | 0,22 | 0,04 | 0,34 | 0,02 | 0,23 | 0,85
 | Travel time (h) | 253,43 | 263,95 | 236,22 | 267,93 | 231,00 | 1252,53
Emissions | C02 (tn) | 5,09 | 5,81 | 4,78 | 5,59 | 5,13 | 26,40
 | N0X (Kg) | 23,66 | 30,94 | 27,05 | 31,77 | 27,85 | 141,26
 | PM (Kg) | 1,63 | 1,17 | 0,53 | 0,58 | 0,87 | 4,78
Noise (db) |  | 89,01 | 93,87 | 93,40 | 93,38 | 92,34 | 92,40
Off-peak
10:00h-14:00h

## Slide 32
Assessment: Indicators
VARIABLE SPEED
CURRENT
Hora Vall
10:00h-14:00h
Off-peak
10:00h-14:00h
Chart: Density (veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 18.682 | 14.8609 | 12.5622 | 13.8616 | 8.9943 | 13.7922
Amb sistema VSL | 18.8245 | 15.0887 | 12.6933 | 13.903 | 8.9469 | 13.8913
Chart: Speed (km/h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 74.6665 | 92.5248 | 96.3089 | 96.8369 | 93.0181 | 90.6711
Amb sistema VSL | 74.3079 | 92.028 | 95.8177 | 96.6018 | 93.0703 | 90.3651
Chart: N0X (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 23.3739 | 30.6985 | 26.9063 | 31.7376 | 27.8056 | 140.522
Amb sistema VSL | 23.656 | 30.9417 | 27.0474 | 31.7666 | 27.8469 | 141.2587
Chart: C02 (tn)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 5.0082 | 5.7504 | 4.7503 | 5.5777 | 5.1248 | 26.2113
Amb sistema VSL | 5.0886 | 5.8086 | 4.781 | 5.5879 | 5.131 | 26.3971
Chart: PM (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 1.5492 | 1.1362 | 0.52289 | 0.57511 | 0.86334 | 4.6468
Amb sistema VSL | 1.6261 | 1.1727 | 0.53142 | 0.58218 | 0.86505 | 4.7775
Chart: Average queue (veh)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 0.063935 | 0 | 0.10241 | 0 | 0.058854 | 0.2252
Amb sistema VSL | 0.085694 | 0 | 0.098108 | 0 | 0.067795 | 0.2516
Chart: Stops (#/veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 0.04126 | 0 | 0.022913 | 0 | 0.026356 | 0.090529
Amb sistema VSL | 0.052977 | 0 | 0.021595 | 0 | 0.028748 | 0.10332
Chart: Travel time (h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 251.5079 | 260.7924 | 233.7046 | 267.1694 | 231.0019 | 1244.1762
Amb sistema VSL | 253.4313 | 263.9511 | 236.2216 | 267.9299 | 230.995 | 1252.5289

## Slide 33
Assessment: Results
DENSITY (veh/km)
SPEED (km/h)
VARIABLE SPEED
CURRENT
Peak Hour Evening
14:00h-20:30h
1
2
5
4
3

## Slide 34
Assessment: Conclusions
No VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Average queue (veh) | 19,65 | 30,47 | 11,80 | 0,00 | 1,36 | 63,29
 | Lane changes | 3,48 | 4,95 | 3,05 | 2,48 | 3,64 | 17,59
 | Number of stops | 6,25 | 9,51 | 4,08 | 0,00 | 0,29 | 20,14
 | Stop time (s) | 47,03 | 81,97 | 37,15 | 0,00 | 4,42 | 170,58
 | Travel time (h) | 1092,44 | 1423,01 | 843,77 | 456,19 | 433,56 | 4248,96
Emissions | C02 (tn) | 29,96 | 38,18 | 19,41 | 10,35 | 10,99 | 108,90
 | N0X (Kg) | 90,65 | 110,79 | 71,21 | 57,37 | 56,93 | 386,95
 | PM (Kg) | 18,70 | 23,33 | 9,47 | 1,42 | 2,61 | 55,54
Noise (db) |  | 89,83 | 94,05 | 93,66 | 94,13 | 92,15 | 92,76
VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Average queue (veh) | 13,86 | 19,30 | 1,50 | 0,00 | 1,31 | 35,97
 | Lane changes | 3,25 | 4,95 | 3,16 | 3,07 | 3,87 | 18,31
 | Number of stops | 4,51 | 6,74 | 0,72 | 0,00 | 0,31 | 12,28
 | Stop time (s) | 33,55 | 53,03 | 4,88 | 0,02 | 4,27 | 95,74
 | Travel time (h) | 913,80 | 1228,82 | 772,90 | 608,51 | 462,51 | 3986,53
Emissions | C02 (tn) | 24,97 | 27,98 | 10,96 | 10,30 | 10,16 | 84,37
 | N0X (Kg) | 80,02 | 87,18 | 46,42 | 50,08 | 50,87 | 314,56
 | PM (Kg) | 14,89 | 15,94 | 3,68 | 1,78 | 2,41 | 38,69
Noise (db) |  | 89,74 | 93,96 | 93,65 | 93,96 | 92,08 | 92,68
In this case, the algorithm does not avoid reaching high densities but delays when they appear.
Taking a look to the indicators, the impact is similar to the morning peak hour. Traffic performance is improved in sections close to Barcelona while it worsen in the rest of sections.
Again, there is a significant overall benefit in terms of travel time and reduction of emissions is also relevant (lower than during the morning).
Peak Hour Evening
14:00h-20:30h

## Slide 35
Assessment: Indicators
VARIABLE SPEED
CURRENT
Peak Hour Evening
14:00h-20:30h
Chart: Density (veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 49.9796 | 49.7941 | 23.8668 | 14.575 | 10.4865 | 29.7404
Amb sistema VSL | 41.6846 | 42.8929 | 24.9476 | 19.4596 | 11.0996 | 28.0169
Chart: Speed (km/h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 37.2239 | 57.688 | 82.6554 | 97.9387 | 94.4509 | 73.9914
Amb sistema VSL | 45.6942 | 54.0702 | 61.9768 | 76.7478 | 89.1172 | 65.5212
Chart: N0X (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 90.6513 | 110.7865 | 71.2148 | 57.3717 | 56.9251 | 386.9495
Amb sistema VSL | 80.0181 | 87.1774 | 46.416 | 50.085 | 50.8678 | 314.5643
Chart: C02 (tn)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 29.9637 | 38.1838 | 19.4104 | 10.3528 | 10.9924 | 108.903
Amb sistema VSL | 24.9748 | 27.9785 | 10.9609 | 10.2987 | 10.1553 | 84.3681
Chart: PM (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 18.6985 | 23.3307 | 9.4745 | 1.4216 | 2.61 | 55.5354
Amb sistema VSL | 14.886 | 15.9392 | 3.6794 | 1.7756 | 2.4062 | 38.6864
Chart: Average queue (veh)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 19.6512 | 30.4725 | 11.7989 | 0 | 1.3627 | 63.2853
Amb sistema VSL | 13.8609 | 19.3017 | 1.5032 | 0 | 1.3074 | 35.9732
Chart: Stops (#/veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 6.2529 | 9.5117 | 4.0786 | 0 | 0.29243 | 20.1356
Amb sistema VSL | 4.5113 | 6.7388 | 0.72216 | 0 | 0.30573 | 12.2779
Chart: Travel time (h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 1092.4363 | 1423.0075 | 843.7735 | 456.1907 | 433.5553 | 4248.9634
Amb sistema VSL | 913.7971 | 1228.8195 | 772.8987 | 608.5071 | 462.5058 | 3986.5281

## Slide 36
Assessment: Results
DENSITY (veh/km)
SPEED (km/h)
VARIABLE SPEED
CURRENT
Night Time
20:30-00:00h
1
2
5
4
3

## Slide 37
Assessment: Conclusions
No VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Average queue (veh) | 1,43 | 0,27 | 0,00 | 0,00 | 0,35 | 2,05
 | Lane changes | 2,02 | 2,31 | 1,58 | 1,69 | 3,29 | 10,90
 | Number of stops | 0,87 | 0,16 | 0,00 | 0,00 | 0,15 | 1,18
 | Stop time (s) | 5,99 | 1,22 | 0,04 | 0,00 | 2,12 | 9,37
 | Travel time (h) | 159,26 | 132,66 | 115,60 | 132,18 | 117,78 | 657,47
Emissions | C02 (tn) | 3,55 | 2,92 | 2,47 | 2,83 | 3,21 | 14,98
 | N0X (Kg) | 15,73 | 17,31 | 15,73 | 17,97 | 18,01 | 84,75
 | PM (Kg) | 1,24 | 0,43 | 0,17 | 0,19 | 0,62 | 2,64
Noise (db) |  | 89,00 | 93,58 | 93,35 | 93,55 | 91,82 | 92,26
VSL |  | Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Traffic | Average queue (veh) | 0,05 | 0,00 | 0,00 | 0,00 | 0,37 | 0,43
 | Lane changes | 2,01 | 2,19 | 1,63 | 1,71 | 3,32 | 10,87
 | Number of stops | 0,05 | 0,00 | 0,00 | 0,00 | 0,17 | 0,21
 | Stop time (s) | 0,23 | 0,01 | 0,04 | 0,00 | 2,24 | 2,52
 | Travel time (h) | 132,64 | 132,37 | 123,51 | 137,40 | 119,61 | 645,52
Emissions | C02 (tn) | 2,60 | 2,80 | 2,49 | 2,82 | 3,17 | 13,87
 | N0X (Kg) | 13,36 | 17,07 | 15,32 | 17,55 | 17,61 | 80,90
 | PM (Kg) | 0,50 | 0,27 | 0,17 | 0,17 | 0,60 | 1,72
Noise (db) |  | 89,00 | 93,42 | 93,17 | 93,39 | 92,04 | 92,20
Analogous behavior to the off-peak interval.
After transition from the evening peak-hour, the algorithm remains inactive due to the low density.
Night Time
20:30-00:00h

## Slide 38
Assessment: Indicators
VARIABLE SPEED
CURRENT
Night Time
20:30-00:00h
Chart: Speed (km/h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 71.042 | 97.6056 | 100.6431 | 100.4212 | 96.1357 | 93.1695
Amb sistema VSL | 76.7562 | 97.0912 | 96.3838 | 97.7694 | 95.2285 | 92.6458
Chart: Density (veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 13.4921 | 8.7707 | 7.2021 | 7.613 | 5.0915 | 8.4339
Amb sistema VSL | 11.2382 | 8.5614 | 7.6446 | 7.924 | 5.0297 | 8.0796
Chart: N0X (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 15.7272 | 17.3103 | 15.7308 | 17.9681 | 18.0096 | 84.746
Amb sistema VSL | 13.3649 | 17.0657 | 15.3168 | 17.5453 | 17.6072 | 80.9
Chart: PM (Kg)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 1.2408 | 0.42523 | 0.17178 | 0.18757 | 0.61796 | 2.6434
Amb sistema VSL | 0.50093 | 0.27252 | 0.17129 | 0.17291 | 0.59955 | 1.7172
Chart: C02 (tn)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 3.5532 | 2.9195 | 2.4742 | 2.8259 | 3.2069 | 14.9796
Amb sistema VSL | 2.5955 | 2.7971 | 2.4861 | 2.8184 | 3.1689 | 13.866
Chart: Average queue (veh)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 1.4304 | 0.26771 | 0 | 0 | 0.3501 | 2.0483
Amb sistema VSL | 0.054762 | 0 | 0 | 0 | 0.37198 | 0.42675
Chart: Stops (#/veh/km)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 0.86591 | 0.16084 | 0 | 0 | 0.15259 | 1.1793
Amb sistema VSL | 0.047248 | 0 | 0 | 0 | 0.16748 | 0.21473
Chart: Travel time (h)
| Tram 1 | Tram 2 | Tram 3 | Tram 4 | Tram 5 | Total
Sense sistema VSL | 159.255 | 132.6588 | 115.6009 | 132.1767 | 117.7824 | 657.4738
Amb sistema VSL | 132.6395 | 132.3651 | 123.5074 | 137.4004 | 119.6116 | 645.5239

## Slide 39
Assessment (Summary)

## Slide 40
Assessment: Economical impact
TOTAL DAY | 16.427 €
TOTAL YEAR * | 3.285.477 €
(*) Approx.. 200 days per year with the same traffic behavior than the simulated
Unit costs from the Handbook on the external costs of transport (EU):
CO2: 100€ / tn
NOX: 6.8€/kg (average between CITY and RURAL scenario)
PM: 348€/kg (for EXHAUST in METROPOLITAN scenario)
Value for time: 12.1€/h (for SHORT DISTANCE and COMMUTER)

## Slide 41
Alternative

## Slide 42
20
20
XX
Maximum static
XX
Minimum dynamic >=
This variant of the algorithm works the same way but adding a new constraint (minimum value for the speed that is set dynamically).
Dynamic speed can’t be lower than a half of the speed without VSL (i.e., for roads with 120km/h of maximum speed, the system can’t propose speeds lower than 60km/h)  Spanish traffic regulations.
2
Hypothesis for the speed

## Slide 43
Assessment: Economical impact
Comparison of indicators (difference): CURRENT vs VSL |  |  |  |  | Unit Cost | Daily benefit
Indicator | PHM | O-P | PHE | NT |  | 
Travel time (h) | 32,69 | -2,87 | 46,04 | 17,37 | 12,1 €/h | 1.128 €
C02 (tn) | 7,44 | -0,29 | 11,36 | 0,98 | 100 €/tn | 1.949 €
N0X (Kg) | 24,64 | -1,39 | 38,26 | 3,21 | 6,8 €/kg | 440 €
PM10 (Kg) | 5,76 | -0,21 | 8,32 | 0,81 | 348 €/kg | 5.105 €
TOTAL DAY | 8.622 €
TOTAL YEAR * | 1.724.444 €
(*) Approx.. 200 days per year with the same traffic behavior than the simulated
Unit costs from the Handbook on the external costs of transport (EU):
CO2: 100€ / tn
NOX: 6.8€/kg (average between CITY and RURAL scenario)
PM: 348€/kg (for EXHAUST in METROPOLITAN scenario)
Value for time: 12.1€/h (for SHORT DISTANCE and COMMUTER)

## Slide 44
AP-7
Comparison between simulations
Simulation 1
20
120
20
120
20
80
20
120
20
120
120
20
50
20
100
20
80
20
60
20
40
20
40
20
40
C-58
Nus Trinitat
Meridiana
1.500 m
1.600 m
1.375 m
1.400 m
1.125 m
5
4
3
2
1
20
100
20
80
20
60
20
60
20
60
20
40
C-58
Nus Trinitat
Meridiana
100
20
80
20
80
20
50
20
80
20
50
20
80
Simulation 2
Simulation 1
Simulation 2

## Slide 45
Video demo

## Slide 46
A research group of:
Thank you!
Francisco Rodero
francisco.rodero@upc.edu