## Slide 1: Data collection and management for traffic management
A research group of:
26th of July 2023
SMART Ankara Sustainable Urban Mobility Plan Contract No. NEAR/ANK/2021/EA-RP/0124
Paco Gasparín
Sergi Saurí

## Slide 2: Agenda
Time | Title/activity
09:30-10:00 | Arrival and registration
10:00-10:05 | Introduction to agenda and the training
10:05-11:00 | Principals of traffic management. The role of ITS on improving urban mobility
11.00-11:20 | Data collection and management for traffic management
11.20-11:30 | Break
11:30-12:30 | ITS solutions for improving traffic in cities
12:30-13:30 | Lunch
13:30-14:00 | Exercise to motivate the topics: what new ITS solutions can be adopted in Ankara?
14:00-14:45 | The implementation of a technological project
14:45-15:00 | Break
15:00-15:50 | Workshop on implementing an ITS project in Ankara
15:50-16:00 | Questions and Closing Remarks

## Slide 3: Data collection

## Slide 4: Data collection
Based on different types of surveys:
  Household household survey
  Individual household survey
  Intercept survey or external cordon
  Intercept surveys, internal cordons and screen lines
  People and vehicle counts
  Travel time surveys
  Stated preference surveys
Traditional methods for mobility patterns
Sensor data collection:
  Electromagnetic loops
  Pneumatic tube
  Piezoelectric sensor
  Fibre optic sensor
  Geomagnetic sensor
  Microwave radar
  Laser sensors
  Ultrasonic sensors
  Bluetooth sensors
  Machine vision cameras
Current methods
Artificial Intelligence
5G and V2X
Mobile phone
Fleet tracking
Smart transportation card
Social network

## Slide 5: Traffic data collection systems

## Slide 6: 1. Variables
Traffic intensity is the number of vehicles passing through a fixed section of road per unit of time. The most commonly used units are vehicles/hour (hourly intensity) and vehicles/day (daily intensity). It is the most important traffic characteristic, as the others are related to it, and provides a very intuitive description of traffic behaviour at any given time. Generally the measurement period is one year, and the average daily intensity (ADI) is the most commonly used magnitude to characterise any road. It is defined as the total number of vehicles passing through a section in a year divided by 365 days.
Intensity
Chart IMH crossroads Barcelona
Chart IMD Spanish radials

## Slide 7: 1. Variables
Traffic density is the number of vehicles per unit length. It can be obtained from a photograph and by counting vehicles, but it is rarely measured directly as it can be easily calculated from measures of intensity and speed (quantities for which it is easier to obtain data). There is a maximum density value obtained when all vehicles are standing in a row, with no gaps between them. This maximum density will be equal to the product of the inverse of the average vehicle length times the number of lanes. Under these conditions, it would be impossible for vehicles to move even at low speeds without colliding with each other.
Density
K = density
N = number of vehicles
D = distance
OCCUPANCY is derived directly from density and is the ratio of the length occupied by vehicles at a given time to the total length of available lanes. Therefore, its value would be equal to the density times the average length of vehicles.

## Slide 8: 1. Variables
A 30 m stretch of road with 3 lanes, occupied by 8 vehicles with a length of 4.5 m, is schematically represented. Under these conditions, the length occupied by the vehicles is 8 - 4.5 = 36 m., while the available lane length is 3 - 30 = 90 m. The occupancy is therefore 40% (36 / 90 = 0.4).
The density of this stretch of road is:
Density / occupancy (example)
which, if multiplied by the average length of vehicles (4.5 metres = 0.0045 km), gives: 88.88veh/ km.⋅ 0.0045 = 0.4 or, in other words, an occupancy rate of 40 %.
It is clear then that occupancy and density are directly related. However, the determination of occupancy as a percentage of the occupied lane in relation to the available lane length presents the same difficulties as the determination of density, as it could only be determined through zenithal photographs of the sections. An easier measure to determine is the % of time that sensors installed on the carriageway detect the presence of a vehicle on them in relation to the total time.

## Slide 9: 1. Variables
Speed forms, together with intensity and density, the group of the three essential variables of any traffic study and it is easy to relate them in such a way that one of them can be obtained from the other two. It is easy to relate them in such a way that one of them can be obtained from the other two. It is usually expressed in km/h and it is necessary to differentiate between:
Point/instantaneous speed: speed calculated on such a short section that it is considered point (Doppler radar, double loop...).
Average speed: speed averaged over a given length based on the calculation of travel time (Bluetooth, radar section...).
Speed
Average speed
Instantaneous speed

## Slide 10: 1. Variables
Intensity, speed and density are related from the fundamental traffic relationship:
Fundamental traffic diagram
The maximum value of the intensity represents the capacity of the road, and the corresponding density is known as the critical density. The range of values in which the intensity increases as the density increases is representative of a more or less fluid traffic in which if there is a small disturbance that momentarily increases the density, it tends to dissipate and return to the previous situation; the traffic is then said to be stable. In contrast, when the intensity decreases as the density increases, it is a sign of an unstable traffic in which there are constant stops and starts.
Vme es la velocidad media espacial (velocidad media de todos los vehículos que en un instante determinado están dentro de un tramo de vía)

## Slide 11: 1. Variables
The classification of the type of vehicle circulating on the road is a piece of information that is usually acquired with different precisions depending on the purpose.
The most rudimentary equipment can make a simple distinction between light and heavy vehicles based on an estimation of length, and this data is often used to make a forecast of road surfacing campaigns.
More advanced equipment can detect multiple vehicle categories based on country classification tables. This data is commonly used in toll systems.
Classification
The FHWA 13 (Federal Highways Administration) system is a commonly used example in the United States for vehicle classification.

## Slide 12: 2. Acquisition systems
The types of sensor used for data acquisition are classified as intrusive and non-intrusive. Intrusive sensors are generally cheaper in terms of installation, however, they have a number of drawbacks:
  Traffic disruption during installation and repair.
  Errors can occur if road conditions are unsuitable.
  Resurfacing of motorways may require re-installation.
NON-intrusive sensors do not directly interfere with traffic during operation, as they are placed on or at the side of the carriageway. As a disadvantage, they are generally more expensive, both the sensors themselves and the installation of the sensors. The non-intrusive detectors currently used are mainly of two types:
  Active sensors: those that emit a signal and capture the response reflected on the vehicle. These include microwave radar, laser radar and ultrasonic sensors.
  Passive sensors: this type of sensor captures variations produced, in certain parameters, by the passage of a vehicle. Passive sensors are for example video cameras.

## Slide 13: 2.1 INTRUSIVE procurement systems
Magnetic loops are the most widespread sensors on Spanish roads as they are a cheap and highly developed technology, with a simple operation that is not affected by environmental conditions.
As with the rest of the intrusive sensors, their disadvantage is the need for installation and repair works. In addition, they are prone to failures and malfunctions in practice, so new technologies are increasingly being sought to replace them. Their operation is based on the variation of the impedance recorded in the loop as a vehicle passes over it.
This technology can detect variables such as INTENSITY, OCCUPANCY, SPEED or determine the CLASSIFICATION of the vehicle using a single or double configuration.
Electromagnetic loops

## Slide 14: 2.1 INTRUSIVE acquisition systems
This type of detector is very useful in temporary or short-term installations, as the rubber tubes are easily placed on the road and the meter is powered by a battery. The most frequent faults that occur are electrical failures of the meter and breakages of the rubber tubes, which have to withstand the impact of vehicle wheels.
With this technology it is possible to obtain different variables such as the INTENSITY, the SPEED (using the double tube referred to above) and the CLASSIFICATION (based on the number and spacing between axles) of the vehicle (light/heavy).
Pneumatic tube

## Slide 15: 2.1 INTRUSIVE acquisition systems
The detection is based on the pressure generated by the vehicle passing over them. They detect the passage of the vehicle based on the electrical charge generated in the piezoelectric material when it is stepped on by a wheel and deforms. They are placed on the road surface and are therefore suitable for mobile measurements. Like rubber tubes, they require amplifiers in the detector to amplify the electrical signal generated. They offer advantages over rubber tubes in that they are more resistant and, being thinner, have less effect on driving.
With this technology it is possible to obtain different variables such as INTENSITY, SPEED, vehicle WEIGHT and vehicle CLASSIFICATION (light/heavy). Some systems combine piezoelectrics with rubbers (i.e. Diamond Traffic) but the main use of this type of sensors is vehicle weighing.
Piezoelectric sensor

## Slide 16: 2.1 INTRUSIVE acquisition systems
They base detection on the pressure exerted by the vehicle passing over the sensor. When a vehicle passes over the detector, the optical transmittance decreases. This variation is interpreted by an opto-electronic interface which determines the presence of a vehicle and even the type of vehicle involved.
The main parameter of these sensors is sensitivity. It can detect anything from objects weighing a few grams to heavy vehicles. These sensors can measure variables such as INTENSITY, vehicle weight and CLASSIFICATION (based on number and axle spacing). They are frequently used in toll systems.
Fibre optic sensor

## Slide 17: 2.1 INTRUSIVE acquisition systems
Unlike coils, magnetic sensors are passive elements that detect the presence of a ferromagnetic metal (by extension the presence of a vehicle) through the disturbance it causes in the earth's magnetic field. This disturbance is known as a magnetic anomaly.
This type of sensor can collect INTENSITY, SPEED and CLASSIFICATION data according to configuration on the ground. A Gateway is required in a nearby area to receive the data they generate wirelessly.
Geomagnetic sensor

## Slide 18: 2.2 NON-INTRUSIVE acquisition systems
Vehicle detection by RADAR is achieved through the emission of a microwave signal (between 1 and 30 GHz, typically 10.525 GHz). The microwaves are reflected by objects and the radar calculates the time elapsed between the emission of the signal and the reception of the reflected signal.
This travel time is the basic variable from which information about the vehicle is extracted. As a main feature, information (INTENSITY, SPEED and RATING) can be extracted from multiple lanes with a single sensor (up to 22 lanes in Wavetronics for example).
Microwave radar

## Slide 19: 2.2 NON-INTRUSIVE acquisition systems
Vehicle detection by laser radar, also known as LIDAR, is performed by emitting a laser light pulse (in the near infrared) to measure the distance to a given object. To calculate this distance, the time taken for the light pulse to travel from the LIDAR to the vehicle and back is measured.
Its traditional use has been to classify vehicles based on their length and volume. Modern LIDAR sensors offer 2D and even 3D images increasing the reliability of vehicle classification. It is commonly used in toll systems or where high accuracy in vehicle classification is required.
Laser sensors

## Slide 20: 2.2 NON-INTRUSIVE acquisition systems
Ultrasonic sensors transmit sound waves at a frequency between 25 and 50 kHz, always above the human hearing range. They are currently rarely used on Spanish roads, as there are more reliable options. The main advantage is their low cost. They generate data on INTENSITY and SPEED.
A typical installation diagram can be seen in the following figure with an example of installation on the road and on the side of the road.
Ultrasonic sensors

## Slide 21: 2.2 NON-INTRUSIVE acquisition systems
This type of sensor takes advantage of the fact that each Bluetooth device (telephones, handsfree devices, etc.) has a unique MAC address that is assigned to it during manufacture and cannot be modified. These addresses, captured by antennas locally, allow, if we have several sensors, to generate data.
The data from the devices is transmitted in real time to a central server where advanced algorithms filter out unwanted detections such as parked vehicles or buses. The data obtained can be used to measure travel time and calculate the average speed of each vehicle on specific stretches, as well as to generate OD matrices.
Bluetooth sensors

## Slide 22: 2.2 NON-INTRUSIVE acquisition systems
Video systems were introduced in motorway management for remote surveillance by a physical operator. However, machine vision techniques are now used to automatically extract different types of information.
The scope of application of cameras has increased, and they are used not only for surveillance, but also for vehicle detection and counting and vehicle identification by automatic number plate extraction, among other things.
Artificial vision cameras

## Slide 23: 2.3 Artificial Intelligence
Technological advances in various fields such as machine learning, Big Data and connectivity have made AI's performance, accessibility and cost feasible for adoption. The nature of the mobility and transport sector (network-based) provides a natural framework and a good opportunity to implement and scale AI.
Machine Learning, ML
The computing technique that allows AI systems to automatically learn and improve from experience without the need to be explicitly programmed.
Deep Learning, DL
It is based on the use of artificial neural networks with many hidden layers that implement progressive abstraction processes on the data, learning more and more general attributes at each level. DL-based AI systems can not only learn concepts, but also recognise complex contexts and shapes, such as image recognition and parity recognition, among others.

## Slide 24: 2.3 Artificial Intelligence
Machine learning (ML) is the older and simpler of the two technologies. It works with an algorithm that the system itself adapts after receiving feedback from a person. In other words, this technology requires feeding the system with structured and categorised data, so that it can deduce how to classify new data of that type. Then, depending on the classification, the system performs certain programmed actions. For example, it identifies whether a dog or a cat appears in the photos and moves the files to different folders.
After the initial application phase, the algorithm is optimised by human feedback, which informs the system of possible misclassifications.system of possible misclassifications and how to assign categories correctly
.Deep learning (DL), on the other hand, does not require structured data. It works with multilayer neural networks, which mimic the behaviour of the human brain and combine different algorithms, allowing the system to process even unstructured data.
Deep learning vs maching learning

## Slide 25: 2.3 Artificial Intelligence

## Slide 26: 2.3 Artificial Intelligence
One of the most relevant functionalities of ML is the automatic recognition of patterns such as, for example, tracking or recognition of different objects in an image: cars, motorbikes, bicycles, pedestrians... The field of pattern recognition refers to the automatic discovery of regularities in data using computer algorithms and the use of these regularities to perform actions such as classifying data into different categories and making decisions.
Use case: Improved machine vision

## Slide 27: 2.3 Artificial Intelligence
Use Case: Urban Risk Detection

## Slide 28: 2.3 Artificial Intelligence
USE CASE: Detection of inter-city risks

## Slide 29: 2.4 5G y V2X
DSRC (G5)
Dedicated Short Range Communications (DSRC) is short to medium range wireless communications designed specifically for automotive use. It provides communications between the vehicle and the infrastructure. This technology works in the 5.9 GHz band and is based on the IEEE 802.11p standard, an extension of the WiFi standard for data exchange in vehicles moving at high speed.
This type of communication offers high data transfer rates, short to medium range (less than 1 km) and low delay. It works with vehicle speeds above 100 km/h.
The combination of this technology with a GNSS system in a vehicle, completely revolutionises the world of traffic data, being able to locate in real time any vehicle or person and know its speed or other parameters that it can provide: emergency braking, airbag activation, occupation...
V2X (Vehicle to everything)

## Slide 30: 2.4 5G y V2X
C-V2X (5G)
Many car manufacturers are incorporating C-V2X connectivity into their vehicles because it has several advantages over DSRC for vehicle-to-vehicle communications, with other manufacturers opting for hybrid interfaces (5G and DSRC) that converge on a single V2x stack.
The main advantages of C-V2X are:
  Providing proven levels of security, range, latency and reliability that far exceed the capabilities of DSRC.
  Leverage the wide coverage of secure and well-established LTE networks, reducing the amount of roadside infrastructure that needs to be installed in both urban and rural areas.
  Enable highly reliable, real-time communication at high speeds and in high-density traffic.
  Support short- and long-range transmissions between vehicles and roadside infrastructure.
  Leverage 5G networks to support autonomous driving, in addition to 4G compatibility.
  Leverage the robust security built into cellular networks.
V2X (Vehicle to everything)

## Slide 31: 2.4 5G y V2X
Types of communication
V2X (Vehicle to everything)

## Slide 32: 2.4 5G y V2X
MOST COMMON USE CASES ½
Collision avoidance: Each vehicle on the road could use C-V2X to transmit its identity position, speed and direction. An on-board computer could combine this data with data from other vehicles to build its own real-time map of the immediate environment and alert the driver to any potential collisions.
Platooning: The formation of a convoy in which vehicles are much closer together than can be safely achieved with human drivers, making better use of road space, saving fuel and making freight transport more efficient.
Cooperative driving: By sharing sensor data, vehicles can use C-V2X to work together and minimise disruptions caused by lane changes and sudden braking.
Queue warning: Road infrastructure can use C-V2X to warn vehicles of queues or road works, so they can slow down smoothly and avoid harsh braking.
Emergency services support: C-V2X can be used to warn road users of emergencies heading towards an incident.
Hazard warning: C-V2X can be used to expand a vehicle's electronic horizon so that it can detect hazards in a blind corner, obscured by fog or other obstacles, such as tall vehicles or undulations in the landscape.
V2X (Vehicle to everything)

## Slide 33: 2.4 5G y V2X
MOST COMMON USE CASES 2/2
Increasingly autonomous driving: Together with other sensors and communication systems, C-V2X will play an important role in making vehicles increasingly autonomous.
Road toll collection: designed to reduce congestion and the impact of motorised transport on the environment by reducing emissions.
Avoiding vulnerable road users: by detecting the smartphones of pedestrians and cyclists, C-V2X will help vehicles avoid collision with other road users.
V2X (Vehicle to everything)
Use cases, 5G Barcelona: https://youtu.be/-1QfPYn2g_c

## Slide 34: 2.4 5G y V2X
A reality
V2X (Vehicle to everything)
https://www.youtube.com/embed/Dvtm-QRAXXk

## Slide 35: 2.5 Mobile phone
There are three main sources of data from mobile telephony:
  Call Detail Records (CDRs)
  NETWORK
  Customers

## Slide 36: 2.5 Mobile phone
CDRs are the main source of information, and contain information on the activity of the provider's customers, after going through an anonymisation process.
CDRs include all actions performed on the mobile network; either from mobile devices or other equipment. The actions recorded are mainly calls, text messages and, above all, internet connections.
There are different types of actions for network users. Specifically, information is recorded for three different types of activity performed:
  incoming calls and SMS
  outgoing calls and SMS
  data connection initiations
Call Detail Records (CDRs)

## Slide 37: 2.5 Mobile phone
Information on the technology that the antennas provide to customers - GSM, UMTS, LTE -, geographic information on their location as well as the position of the operator's network antennas in force during the data period analysed - region, province, municipality and locality, address and postcode.
This source is particularly important as it represents the locational component to which the CDRs are associated. The more granularity provided by the network information, i.e. antennas, the better.
Clients
This group of files contains basic information on customers, showing their anonymised identifier, gender, age, average bill amount, contracted tariff and the postal code of the billing address associated with each user.
NETWORK

## Slide 38: 2.6 Fleet tracking
Fleet trajectories are made up of a series of locations that can reflect when and where activities occur and are therefore used to analyze human dynamics.
A better understanding of human dynamics has motivated many studies in transportation management, urban planning, land use modeling, and traffic flow prediction.
These data are collected using a fleet of dedicated cabs equipped with GPS (Global Positioning System) devices.
Methods have been proposed, such as random walk in the case of floating vehicle fleets aimed at real-time monitoring of traffic status, random direction, etc.
To express the spatial distribution of the mobility patterns, the road network is divided into crossing points, generating small pieces of road, called segments...

## Slide 39: 2.6 Smart transportation card
The use of smart cards has become significant because of the development of the Internet and the increasing complexity of mobile communication technologies.
The data generated by smart card systems track the detailed on-board transactions of each cardholder. It is argued that smart card technology can provide valuable information because it is a continuous data collection technique that provides a complete, real-time travel diary for all bus travelers.
Smart card data (SCD) can be used to validate traditional travel models applied to public transportation.
It is claimed that the SCD is a good substitute for household surveys or at least a complement.

## Slide 40: 2.7 Social networks
Location sharing services (LSS) such as Foursquare, Gowalla and Facebook provide hundreds of millions of user-controlled footprints (e.g., "Checkins"). These global-scale footprints provide a unique opportunity to study the social and temporal characteristics of how people use these services and to model human activity that are important factors in the design of future mobile + location services, traffic forecasting, urban planning, new retail locations, as well as epidemiological models of disease spread.
Unlike mobile phone data and trajectories derived from GPS trackers, the checks have several unique characteristics:
  They are inherently social, as users reveal their location to their friends, which means that social structure and its impact on human mobility can be directly observed.
  The checks are associated with specific locations (e.g. a restaurant), which allows for further analysis of the type of location.
  Checks can be augmented with short messages, providing partial insight into the thoughts and motivations of the users of these services.

## Slide 41
A research group of:
Thank you!
Pac Gasparín paco.gasparin@upc.edu
Sergi Saurí sergi.sauri@upc.edu