## Slide 1: ITS solutions for improving traffic in cities
A research group of:
25th of July 2023
SMART Ankara Sustainable Urban Mobility Plan Contract No. NEAR/ANK/2021/EA-RP/0124
Paco Gasparín
Sergi Saurí

## Slide 2: Agenda
Time | Title/activity
09:30-10:00 | Arrival and registration
10:00-10:05 | Introduction to agenda and the training
10:05-11:00 | Principals of traffic management. The role of ITS on improving urban mobility
11.00-11:20 | Data collection and management for traffic management
11.20-11:30 | Break
11:30-12:30 | ITS solutions for improving traffic in cities
12:30-13:30 | Lunch
13:30-14:00 | Exercise to motivate the topics: what new ITS solutions can be adopted in Ankara?
14:00-14:45 | The implementation of a technological project
14:45-15:00 | Break
15:00-15:50 | Workshop on implementing an ITS project in Ankara
15:50-16:00 | Questions and Closing Remarks

## Slide 3: ITS solutions for improving traffic in cities

## Slide 4: 1. Traffic light control

## Slide 5: The traffic regulator
The basic element for automated intervention in urban traffic is the traffic controller, or regulator. This equipment senses lanes, acts on traffic by means of light signals (groups) and regulates flows following cyclical programs (usually).
Protocols
Hardware
Singularities
The regulators communicate through communications protocols.
The basic components of a traffic controller are:
COU card
Group cards
Detector cards
Power supply
Some elements that differentiate a controller from a PLC:
Integrated safety system
Specific signals
Specialized control

## Slide 6: The traffic regulator

## Slide 7: Scheduling and time management
Traffic light groups
A semaphoric group is a combination of one, two or three groups, which govern a movement. Typically, there are:
Vehicle groups:
With three bulbs
(red, amber, green). They regulate the movement of vehicles.
Pedestrian groups: With two lights (red, green). They regulate the passage of pedestrians
Movements
Basically a controller manages the movements in time
To do this, it determines the status of its groups (red, amber, green) according to the hourly population that may or may be not be conditioned by the readings of the detectors
Plans
Regulators have a library of plans. Each plan determines a behavior. The plans can be activated automatically, by indication from the control center, following a schedule, etc.

## Slide 8: Scheduling and time management

## Slide 9: The regulator of the future
Agnostic protocol
It currently makes no sense to limit the connectivity of a device based on its protocol.
Cloud connectivity
New functions
V2X connectivity: It takes control to the next level. Not only is it possible to capture a large amount of new data, but also to intervene in traffic in different ways, affecting driver behavior and anticipating risk situations. risk situations.
EdgeX Node: Allowing the execution of other processes within the hardware itself.
Today's regulators and protocols were designed in the era of wired communications and limited processing capabilities. Today these limitations have been overcome and will affect the way we understand and manage traffic.
Our new Mobility Hub controller connects natively and securely to our SATURNO platform, allowing optimal real-time control and multimodal access (Smartphone, browser, video wall).
The protocol has been developed following cloud connectivity standards, such as API Rest, JSON, HTTPs, MQTTs, as well as the most widespread style standards.
Possibility of scheduling from the cloud, in graphical mode, with resource libraries and plans that are shared by the management system.
Usability

## Slide 10: Centralized traffic management

## Slide 11
The network optimization process
The optimization process is cyclical, with a typical periodicity of 5 to 15 minutes.
It recalculates system parameters and controller settings based on a target. This process can be automatic, manual or guided by preset configurations.
Defines the current traffic situation based on the reading and processing of sensors (loops, VA, gauging, etc.).
It sends the new parameters to the controllers, thus influencing the system to be controlled (traffic).

## Slide 12
Data collection - Basic measurements

## Slide 13
Data collection - Basic measurements
Intensity points
A typical problem is the lack of physical detectors to take measurements. It is not always possible to have adequate sensing to measure all sections of the city. However, it is possible to reduce the number of physical elements by using mathematical or statistical interpolations.
Physical detectors
Measurement points
Capacity points
They correspond to loop or vision sensors. They provide intensity, occupancy and, optionally, speed.
Linear combinations of detectors, allowing extrapolation of measurements to non-detector locations.
These are temporary measurements of a network point, generating a pattern for different situations.
Linear combinations of detectors and capacity points

## Slide 14
Process - Global Strategy
Free mode
Based on the data, and knowing the traffic situation, calculation and action decisions will be made on the basis of a strategy. This strategy can change and is chosen according to the configuration of the system.
Fixed
By network status
By calendar
The operator sets the strategy to be applied
The strategy is determined by the traffic situation.
Logical rules are defined that determine which strategy to activate, depending on the behaviour of lanes, accesses, sections, intersections, travel times, etc.
The strategies follow a scheduled program, which considers the season, the type of day and the time of day.
There is no grouping of controllers by zones or coordination groups.
In this mode the system only monitors, and it is the operator who sends commands to the controllers.

## Slide 15
Process - Distribution and bundling
The most important point in the strategy is to determine how the city will be distributed into zones, which sections will be favoured and which objectives are to be achieved in each area. The most important distribution elements are the zones and the co-ordination groups.
Zone
Coordination group
Zones are disjoint areas that group control elements together and keep them synchronised, so that optimisation algorithms can be applied to them.A city can be grouped into one or several zones. In classical systems, zones are conditioned by communication limitations. In modern systems, zones can be created without any limitations.
A coordination group is a sequence of consecutive junctions over which traffic conditions are intended to be favoured.Coordination groups are the most important elements in traffic flow, as they will determine which lanes will be favoured by the system when setting green times.

## Slide 16: Process - Distribution and bundling

## Slide 17
Process - Optimisation
Once the system has a strategy and zoning, a calculation process begins to determine the optimal parameters for each junction to achieve the overall objectives. The three basic parameters are cycle, distribution and offset.
Cycle
Distribution
Offset
It applies to all regulators in the area. The cycle is determined according to the target to be achieved:
Maximise capacity: Based on a capacity target (Xc): 𝐶ó𝑝𝑡𝑖𝑚𝑜 𝑖 = 𝐿𝑖 𝑋𝑐 (𝑋𝑐 -𝑌𝑖 )
Minimize delays: Delays in critical lanes are reduced 𝐶ó𝑝𝑡𝑖𝑚𝑜 𝑖 = 1.5 𝐿𝑖 + 5 (1-𝑌𝑖 )
Minimise fuel consumption: The aim is to reduce downtime 𝐶ó𝑝𝑡𝑖𝑚𝑜 𝑖 = (1.4 + 𝐾) 𝐿𝑖 +6 (1-𝑌𝑖)
Li: time lost from intersection
It consists of dividing the green time (C-L) of each intersection between its phases.This takes into account the degree of saturation of each critical lane group with respect to the total sum (Y).For phase j of intersection i, the green time corresponding to its critical lane group is:
𝐹
Determines the offset from the start of the cycle. If a regulator has offset n, its first phase will start at the second n of the cycle. The offset is a fundamental variable in order to generate green waves.
Uncoordinated group
Red phases overlap
Crossings have been offset to allow for green waveCoordinated group

## Slide 18
Performance
When the calculation process has been completed, a cycle, split and offset value is available for each crossing. These values are sent via direct communication with each controller. Depending on the technology, this transmission may require intermediate devices.
Classic systems
Improved systems
Modern systems
The controllers are controlled by physical zone controllers, which send the values to each controller, communicating in their native protocol (AENOR M, V, B, NTCIP, OCIT, etc.).their native protocol (AENOR M, V, B, NTCIP, OCIT, etc).
Zone controllers are virtual machines that run on the room servers. This gives more flexibility and makes it possible to create zones without the limitations of classic systems.
The communication protocol with the controller remains a classic protocol.
The controllers are directly connected to the cloud. The actuations are sent directly to the device via agnostic and cyber-secure protocols.

## Slide 19
Performance
Other devices that are commonly integrated into the traffic management system include cameras, number plate readers, bollards and barriers, parking bollards, variable message signs and environmental sensors.

## Slide 20: Classical systems technology

## Slide 21
Control levels
Most of today's management systems have been developed before the emergence of the cloud-computing and edge-computing paradigms. The architectures follow a layered model, with specific protocols and applications or equipment at each level.
Control centre
Zone Centrals
Regulators
They are diverse, connected applications that perform the following functions:
Status monitoring
Plan changes according to time conditions or logic rules
Green wave adjustment
Fluency measurements and calculation of indicators
Communication with zone exchanges)
They are usually physical computers, although it is increasingly common for them to be virtualised.
Their functions are:
Communications hub and media conversion.
Temporary data storage.
Time synchronization in the controllers.
Communication with the controllers.
This equipment is dedicated to the control of one or several crossings, with a specific protocol.
Their functions are:
They regulate signaling, following a cyclical scheme, normally periodic.
They act commanded by the center through the zone control centers, or autonomously.
They collect data from detectors.

## Slide 22
Levels of control
Each layer or tier has specific equipment, capable of operating in isolated mode. This offers a high level of service but creates problems of synchronism and integrity of data and configurations.
Technologies
Zone Centrals
Control centres are n-tier models, with a database layer common to a number of services and applications, typically Windows.
Zone control centres are typically deployed on an industrial PC or on dedicated hardware, usually with a Linux or similar system.
Controllers are specifically designed equipment. Their behaviour depends on the standard they follow. They are usually not compatible.

## Slide 23
Centre software
They usually consist of a backoffice with storage applications and services, plus one or more visualisation applications, from which to operate the system in a user-friendly and graphical way.
Features
The most common in this type ofsoftware is to be found:
Windows applications and interfaces, installed on the operators' computers.
Windows or Linux servers, serving these applications, on the room's servers.
Very limited connectivity from the outside, usually using remote access applications.

## Slide 24
Problems of classical systems
Control centre
Zone Centrals
Regulators
Proprietary and closed software
Great integration difficulties
Any new type of device requires redesign of all layers
They are not really necessary, as nowadays the regulators communicate directly via the network.
They become a critical element (if the sub-centre goes down, its regulators go down).
Protocol incompatibility (AENOR M,V, OCIT, NTCIP, etc).
Control centres are tailor-made for a specific protocol.
It is not possible to combine different types of controllers in the same centralisation.

## Slide 25: Next generation systems

## Slide 26
The turning point
For decades, applications have been built with a high dependency on the operating system, have been installed on local PCs and servers, and have required great integration efforts between them, or it has simply not been possible to integrate them. Today, with cloud computing and SaaS, these barriers have been overcome.
Local computing
Cloud computing
Multiple applications to solve different needs for the same problem.
Operating system and hardware dependent.
Data is captive to each application.
Not intended for remote or multimodal access.
The systems are accessible by standard means (web browser) and are always up to date.
Access is multimodal, without dependence on OS or hardware (tablet, mobile, PC, IoT).
The information is transversal and can be consumed and fed by any third party.

## Slide 27: 2. Low Emission and Access Control Area

## Slide 28: What is LEZ?
An area delimited by an administration which, in the exercise of its powers, progressively restricts access, circulation and parking of vehicles in order to improve air quality and mitigate greenhouse gas emissions.
More than two hundred European cities in ten countries, such as London, Berlin or Paris, have implemented such zones.

## Slide 29: Scope of application
The whole city or the whole metropolitan area
The restriction scheme is initially limited to vehicles without an environmental sticker without any exemption for resident
Small urban areas
Old town centres, central areas or sensitive environments:Schools, residences, hospitals...)
They may have more restrictive traffic criteria and progressive implementation criteria(ultra-low/zero emission zones)

## Slide 30: Vehicle Labelling
High level of public awareness in all countries.
Harmonisation of restrictions.
Legally established system (legal certainty).
Technically robust.
The AMB has established a signage model common to all the ZBEs, which has been adopted by the DGT and is intended to be extended and adapted to all the cities in Spain.
Physical signs have been installed along the entire perimeter of access to Barcelona. These signs have been complemented with approach signs: conventional vertical signs and signs using variable light panels.
Signalling
Labelling of vehicles according to their polluting potential, DGT
Spanish labelling system, similar to that used in Germany and France:

## Slide 31: Systems for the management of low emission zones

## Slide 32: Enforcement system
Capture sub-systems
Enforcement of the LEZ restrictions requires the creation of systems to detect vehicles that are not authorised to circulate and to be able to sanction them.
It is essential that enforcement systems are as automated as possible.
Information sub-systems
Management sub-systems

## Slide 33: Capture subsystem
Multiple optics are required to capture number plate and context video.
Typically "all-in-one" solutions where a single device integrates several cameras, infrared LEDs and image processing unit.
For some years now, cameras have been incorporating algorithms based on Deep Learning neural networks to perform number plate OCR, classify vehicles and make corrections locally.

## Slide 34: A look into the future

## Slide 35: Dynamic urban toll systems
Internal
London, Milan, Singapore and Doha have already deployed urban tolling systems.
The next step is to manage charges dynamically according to pollution episodes.
In order to communicate dynamic changes to drivers, a communication-mix will be used: 5G, V2X, Mass-Media, RRSS, web, Apps, etc.

## Slide 36: Low-cost air monitoring systems
Source: RACC "Analysis of air quality indicators in the Barcelona Low Emission Zone (LEZ)".
Currently air monitoring through networks of official air quality monitoring and forecasting stations (RVPCA).
Efforts are underway to validate IoT systems to distribute thousands of environmental sensors in cities.

## Slide 37
Integration with other city management platforms
Telesto
City Access control
Cloud based traffic Management
Trafic light
controller IoT
Atalante
Fleet management
Data Analytics BIgData
M-Hub
New generation Traffic light controller
SATURNO
Open Smart City Platform
Dione

## Slide 38: Roadmap LEZ
Roadmap LEZ 2020 – 2030 Amsterdam
The LEZ must be integrated into the framework of the sustainable mobility policies of municipalities, metropolitan areas and regions.
A LEZ agenda allows for a progressive evolution from access control zones to zero emission zones.
Cities such as London, Brussels or Amsterdam have established a timetable of progressive restrictions until 2030 or 2050.

## Slide 39
A research group of:
Thank you!
Paco Gasparín francesc.gasparin@upc.edu
Sergi Saurí sergi.sauri@upc.edu