## Slide 1: ITS and traffic management
A research group of:
25th of July 2023
SMART Ankara Sustainable Urban Mobility Plan Contract No. NEAR/ANK/2021/EA-RP/0124
Dr. Sergi Saurí
Frances Gasparín

## Slide 2: Agenda
Time | Title/activity
09:30-10:00 | Arrival and registration
10:00-10:05 | Introduction to agenda and the training
10:05-11:00 | Principals of traffic management. The role of ITS on improving urban mobility
11.00-11:20 | Data collection and management for traffic management
11.20-11:30 | Break
11:30-12:30 | ITS solutions for improving traffic in cities
12:30-13:30 | Lunch
13:30-14:00 | Exercise to motivate the topics: what new ITS solutions can be adopted in Ankara?
14:00-14:45 | The implementation of a technological project
14:45-15:00 | Break
15:00-15:50 | Workshop on implementing an ITS project in Ankara
15:50-16:00 | Questions and Closing Remarks
16:00 | End of the first day of TM4

## Slide 3: Principals of traffic management. The role of ITS on improving urban mobility General concepts of traffic flow Dynamic Speed Limit Traffic Light Optimization Managed lanes MFD, parking policy and access control

## Slide 4: General concept of traffic flow

## Slide 5: Fundamentals traffic flow variables
MLTM - 5
Monotonic smooth approximation of N(t,x)
N
t
Count start time
count section
FLOW
x
t
A
xj _
tj _
Flow
Density
Average speed
Volume, count, traffic, intensity, demand

## Slide 6
FUNDAMENTAL EQUATION
CONTINUITY EQUATION
RELATIONS
It is enough to measure 2 variables:
  Cars (k difficult) 
  Pedestrians (v difficult) 
soft enough

## Slide 7
u
q
C.
A
B.
u c
DESIGN

## Slide 8
q
k
kc _
k j
C.
A
B.
CONTROL
THEORY
K
U
kc _
u c
A
B.

## Slide 9
 | q | v | k
MICRO | INTERVALS | SINGLE SPEED | SPACING (VEHICLE TRACKING)
MACRO | FLOWS | AVERAGE SPEED | DENSITY (SHOCK WAVES)
MICRO and MACRO CHARACTERISTICS

## Slide 10
Urban Queue Networks
LIMITED STORAGE
“ Increasing the capacity of the bottleneck lowers the total flow ”
30 veh.
+1 min
50 veh/min
20 veh/min
?
+1 min
50 veh/min
20 veh/min
30 veh/min
Line
20 vehicles = 1 min
0
1
q
t
t 1
t2
O
D.
1
2
sa Conservation t 1 =t 2 minimizes the hatched area (Wardrop)

## Slide 11
If we increase the capacity of the bottleneck to 40 veh/min, the blocking of the by-pass causes the output flow to be 40 veh/min (=bottleneck). The queue increases to 40 vehicles.
50 veh/min
40 veh/min
0 veh/min
The line grows
40 veh/min
A
Initially, through information, traffic can be captured from A
"Do not allow queues to occur within the system"
The only solution: manage demand upstream

## Slide 12: Dynamic Speed Limit (DSL)

## Slide 13: An overview
 | GERMANY (1965) | HOLLAND (1992) | USA (1962) | AUSTRALIA (1993) | FINLAND (1994) | UNITED KINGDOM (nineteen ninety five) | SWEDEN (2003) | FRANCE (2004)
REDUCE THE ACCIDENT RATE | Reduction of between 20 and 30% of the number of collisions. |  |  | A 7% reduction in the number of collisions |  | 10% reduction in the number of collisions |  | Reduction between 15 and 40%
IMPROVE FLUIDITY |  |  |  |  |  |  |  | Reduced congestion by 16%
REDUCE POLLUTING EMISSIONS |  |  |  |  |  |  |  | 

## Slide 14: Main objectives
Reduce the accident rate
Improve the fluidity of circulation
Reduce polluting emissions
.
Decrease in accidents (10 to 40% depending on implementation).
Confirm the results with longer series of data.
In most cases, improvements in congestion reduction are not appreciated .
Only in France and the Nordic countries there are minimal improvements .
The reduction, in free regime , is corroborated in the cases analyzed.
Higher emissions occur in congested states

## Slide 15: User acceptance level
 | GERMANY (1965) | HOLLAND (1992) | USA (1962) | AUSTRALIA (1993) | FINLAND (1994) | UNITED KINGDOM (nineteen ninety five) | SWEDEN (2003) | FRANCE (2004)
ACCEPTANCE/SATISFACTION |  |  |  |  | 96% are satisfied | 60% are satisfied |  | High degree of satisfaction
USER | better install variable signaling that fixes | Especially in adverse conditions | only if required | It depends if there is compliance control | Behavior is changed when there are signs of danger | only if required |  | 75% respect variable limits

## Slide 16: Conceptual Analysis
K 0 = Critical density (maximum capacity of the road)  It can vary considerably from one day to the next for no apparent reason ( stochastic phenomena )
The diagram is unique to each infrastructure, the distribution of drivers and their driving style
When the density (K) is low  Vehicles circulate at the maximum speed allowed
When K > K 0 inefficient operation (congestion)

## Slide 17: Conceptual Analysis
Limiting the speed in free regimes to the optimal speed or lower
In free regime there is an increase in travel time .
For the same demand, in free regime, the traffic flow will be characterized by a lower speed and a higher density . Hence
When tails do occur they will grow slightly faster due to the higher density of incoming free flow. (Difference in slope between the pink and blue lines).
In very dense states, the variation between speeds is reduced, which improves fluidity ( stop & go reduction ).

## Slide 18: Conceptual Analysis
Limiting the speed below the optimum
Modification of the fundamental diagram .
The maximum capacity of the road is reduced by imposing a speed below the optimum. (If good management is not done, it can be counterproductive).
Reduction of speed variance.

## Slide 19: Conceptual Analysis
Aspects for the strategy to be beneficial:
UNIFORMIZATION OF SPEEDS WITHIN THE CONGESTIONED SECTIONS.
Eliminate speed disturbances to obtain a constant flow and avoid small local restrictions characterized by continuous stops and starts (stop & go ) typical of congested states
GLOBAL MANAGEMENT OF THE CORRIDOR.
Artificial bottlenecks (where speed is limited) can be generated . Therefore, the measure does not eliminate the queues, but it changes their location.
The key is to place them intelligently based on the location of the links and the origin-destination matrices.

## Slide 20: Complementary with other traffic management tools
SPEED UNIFORMIZATION
GLOBAL MANAGEMENT OF THE CORRIDOR
IT ALLOWS:
SYNERGIES:
STOP & GO
DOES NOT ELIMINATE THE QUEUES BUT CHANGES THEM
VERY REDUCED EFFECTS
CONGESTION REDUCTION STRATEGIES
RAMP METERING
ACTIVE LANE MANAGEMENT
USE OF SIDE SIDEWAYS DURING RUSH HOUR
REDUCE THE WIDTH OF THE LANES (according to speed)

## Slide 21: Advantages
+ Improving capacity at bottlenecks
+ Intelligent queue location using VSL (and access control) can bring improvements in motorway efficiency.
+ A limitation in a range between 70 and 90 km/h (depends on the vehicle fleet) reduces emissions in periods of free movement .
+ Significant reduction in the number of accidents and minor injuries , although a longer data series would be necessary.
SPEED UNIFORMIZATION
( STOP & GO REDUCTION)

## Slide 22: Disadvantages
- Non intelligent management can produce disastrous results
- Benefits the links close to the city
(main bottleneck)
- Punctual control ( radar) in predetermined locations does not ensure compliance throughout the section.
- It must be assessed whether the increase in travel time is offset by the reduction in emissions.
LIMITED EFFECTS WITH IMPORTANT SYNERGIES WITH OTHER IMPROVEMENT STRATEGIES IN TRAFFIC MANAGEMENT
CREATE QUEUES WHERE THERE WERE NO QUEUES
PENALIZES LONG ROUTES IN RELATION TO THE LINKS CLOSE TO THE BOTTLE NECK
INDUCE DEMAND ON THESE LINKS.
LOSS OF IMPROVEMENTS AND WORSENING OF THE GLOBAL SITUATION

## Slide 23: Managed lanes

## Slide 24: Managed lanes
Managed Lanes are the strategies which package lanes depending on;
  criteria (e.g. vehicle destination, occupancy or qualification)
  purposes (e.g. reduce lane changes, optimize the use of the lanes, improve the level of service for carpool vehicles)
Managed Lanes can facilitate traffic flow in response to changing conditions (i.e. variation on the on/off ramp demand, special events, work zones or incidents) by controlling user eligibility, access (by pricing or destination discrimination) and lane assignment.
Traditional lane management strategies include;
  High occupancy vehicle (HOV) lanes
  High occupancy toll (HOT) lanes
  Dynamic lane assignment (DLA)

## Slide 25: Strategy for HOT (High Occupancy Tolls) and HOV (High Occupancy Vehicles) lanes
Concept:
The primary purpose of an HOV lane is to increase the total number of people moved through a congested corridor by offering two kinds of incentives to the users:
  travel time savings
  reliability and predictability travel time
HOT lanes allow single or lower occupancy vehicles to use an HOV lane for a fee, while maintaining free travel for qualifying HOVs and green vehicles.
Examples:
Bus-only roadways
Freeway lanes reserved for HOVs
Bypass lanes at metered freeway entrance ramps
Special lanes on arterial streets
Technology:
Non-separated HOV facilities share the right of way with general purpose lanes.
Separated HOV facilities are separated from general purpose lanes by physical barriers or a buffer space. The barriers might be temporary or permanent.

## Slide 26: Strategy for HOT and HOV lanes
Experiences
The opening of the bus-only lane on the Shirley Highway in Northern Virginia/Washington, D.C. in 1969 represent the first freeway HOV application in the U.S.
HOV lanes are currently operating in Europe and Australia. Madrid, Linz, Leeds, Amsterdam, Stockholm, Oslo
The C58 in the north access to Barcelona are the main projects to date.
By introducing HOV lane in Madrid case study the public transport mode share grew from 23% to 35% after implementation, while single occupancy vehicle use dropped from 70% to 48%.
For HOT Lanes;
  Multiple variations in pricing application (dynamic, e.g. I-95 Miami; flat rate, e.g. I-15 Salt Lake City; or time-of-day rating, e.g. I-25 Denver)
  Access (occupancy, e.g. SR-167 Seattle; green-vehicles class, e.g. I-15 San Diego; or midway accessibility, e.g. I-10 W Houston) are found throughout the U.S.

## Slide 27: Dynamic lane assignment
Concept:
DLA strategies try to address one of the most disrupting activities of freeway traffic: lane changes and the indiscriminate use of each one of the lanes based only on the drivers self criteria, with neither information nor control. Commonly, drivers try to maximize their own benefit without considering the efficient performance of the whole system.
Technology:
Off-Ramps
  Increase the off-ramp capacity by using the hard shoulder,
  Queue the vehicles that want to exit in a specifically reserved lane in order to avoid last-minute incorporations
  Ban lane changing immediately before and after the problematic off-ramp.
  Avoid underuse of alternative off-ramp(s).
On-ramps
  Free flow traffic in the entrances by lane-changing prohibition during peak hours for right lane(s) upstream problematic entrances.

## Slide 28
Experience:
In France, hard shoulder running was introduced in 2000 near Paris, where two urban freeways (A4 and A86) share a 2.3 km-long weaving section.
In Great Britain, an operational scheme using the hard shoulder along 17 km on the M42 three-lanes freeway close to Birmingham became operational in 2006 with increased the observed freeway capacity by an average of 7%.
opened to traffic hard shoulder lane in the A4-A86 concurrent freeway (France)
hard shoulder in the M42 freeway (Great Britain)

## Slide 29: Ramp metering
Concept:
Short delays at on-ramps is the relatively low price to pay for maintaining capacity flow on the freeway itself, leading to substantial savings for each individual road user.
Technology:
RM strategies may be classified according to various characteristics:
Real time strategies; base their decisions on collected real-time measurements from the freeway mainstream and the on-ramps
Local strategies; control individual on-ramps based on real-time measurements collected in the vicinity of the on-ramp.
Coordinated strategies; control all metered ramps of a freeway (network) based on all available real-time measurements.

## Slide 30: How do the ramp meters work?

## Slide 31
Experiences
In Great Britain, the firsts ramp metering were introduced in the junction 10 of the M6 (in Walsall, Birmingham) in 1986.
More than 30 locations (in Leeds, Manchester and Birmingham) with Local RM strategy are currently operational.
Local RM strategy is also operative in several locations in France (i.e. Paris, Lyon and Bordeaux). Local RM strategy is currently operating in more than 100 locations around Germany.
In Auckland, traffic data collected from 25 ramp metering sites in 2007 (before ramp metering) and 2009 (after ramping) showed an average 25% improvement in both congestion duration and traffic speed, and an 8% increase in traffic throughput.
Ramp metering in North Carolina, USA

## Slide 32: Traffic Light Optimization

## Slide 33: An overview
t
# vehicles

1
1

n’
n
r
g
r
A
#
backwards in recovery
stationary front
t
backwards in formation
Average waiting time:

## Slide 34: Street level
Travel time of a bus
Stochastic variables
Deterministic variables
= time in the intersection
= travel time in the section
= waiting time
= travel time in the section
= waiting time
More detail: tomorrow’s session

## Slide 35: MFD, Parking Management and control access

## Slide 36: Macro Fundamental Diagram
Experimentos reales: Yokohama, Japón
Sensores fijos:
500 detectores ultrasonidos
Conteos cada 5 min
Sensores móviles:
140 taxis con GPS
Tiempo, posición, paradas, etc.

## Slide 37: Macro Fundamental Diagram
Experimentos reales: Yokohama, Japón
Sensores fijos:
500 detectores ultrasonidos
Conteos cada 5 min
Sensores móviles:
140 taxis con GPS
Tiempo, posición, paradas, etc.

## Slide 38
Experimentos reales: Yokohama, Japón
MFD

## Slide 39: Application of MFD: Parking Management
Over half the cars driving downtown in cities with serious parking problems are cruising to find a parking (Arnott and Rowse, 1999)
Inefficient parking traffic accounts for up to 30% of total traffic in city centers (Allen, 1993)
Average time to find a curb space for some American cities: 3.5 – 14 min. (Shoup, 2006)

## Slide 40: Application of MFD: Parking Management
Given : inflow qin
Output: e = G(n)
e = G(n)
qin
n
n
Network System
Parking System
Cars
Capacity

## Slide 41: Application of MFD: control access

## Slide 42
A research group of:
Thank you!
Francesc Gasparín Francesc.gasparin@upc.edu
Sergi Saurí segi.sauri@upc.edu