## Slide 1: Geleneksel Ulaşım Modelleri ve Sürdürülebilir Kentsel Ulaşım Projesi (SKUp) Uygulamalarında Kullanılan Yeni Modeller
A research group of:
18 Ekim 2023
SMART Ankara Sürdürülebilir Kentsel Ulaşım Planı Sözleşme No. NEAR/ANK/2021/EA-RP/0124

## Slide 2: Gündem
Saat | Başlık/Faaliyet
09:30-10:00 | Geliş ve Kayıt
10:00-10:05 | Gündemin ve Konu Başlıklarının Tanıtımı
10:05-10:50 | Temel Bilgilere Giriş: 4 Adımlı Modelleme
10:50-11:20 | Modern Yaklaşımlar: Faaliyete Dayalı Modelleme
11.20-11:30 | Ara
11:30-12:00 | Modern Yaklaşımlar: Temsilci Tabanlı Modelleme
12:00-12:30 | SKUp Bağlamında Mikro-Simülasyon
12:30-13:30 | Öğle yemeği
13:30-14:00 | Ulaşım Modellemesi Kullanarak SKUp Politikasının Değerlendirilmesi
14:00-14:45 | Ulaşım Modelleme Alıştırması
14:45-15:00 | Ara
15:00-15:50 | Yük Taşımacılığı Modellemesi
15:50-16:00 | Sorular ve Kapanış Konuşmaları

## Slide 3: Gündem
Saat | Başlık / faaliyet
10:00-10:05 | Gündemin ve Konu Başlıklarının Tanıtımı
10:05-10:50 | Temel Bilgilere Giriş: 4 Adımlı Modelleme
10:50-11:20 | Modern Yaklaşımlar: Faaliyete Dayalı Modelleme
11.20-11:30 | Ara
11:30-12:00 | Modern Yaklaşımlar: Temsilci Tabanlı Modelleme
12:00-12:30 | SKUp Bağlamında Mikro-Simülasyon
12:30-13:30 | Öğle yemeği
13:30-14:00 | Ulaşım Modellemesi Kullanarak SKUp Politikasının Değerlendirilmesi
14:00-14:45 | Ulaşım Modelleme Alıştırması
14:45-15:00 | Ara
15:00-15:50 | Yük Taşımacılığı Modellemesi
15:50-16:00 | Sorular ve Kapanış Konuşmaları

## Slide 4: Temel Bilgilere Giriş: 4 Adım Modeli
Modelleme haritası
4 adımlı modelleme
Geleneksel modellemelerin bazı zayıf yönleri
İnsan davranışının modellenmesinde karmaşıklık ve gerçekçilik

## Slide 5
SKUp Modelleme Araçlarının Amacı
Çok Kriterli Analiz
Beklenen maliyet-fayda analizi
Ekonometrik modeller
Ekonometrik modeller
Nihai maliyet-fayda analizi
Çok Kriterli Analiz
Politika değerlendirmesi (ulaşım modellemesi)

## Slide 6
SKUp bağlamında ulaşım modellerinin kullanımı
Ulaşım modelleri, ulaşım arz ve talebinin ve bunların belirli bir bağlamdaki (örneğin bir şehirdeki hareketlilik) etkileşiminin basitleştirilmiş temsilleridir. Ancak ulaştırma modelleri oluşturmanın amacı mevcut koşulların basit versiyonlarını oluşturmak değildir: ulaştırma modelleri bu mevcut koşullardaki değişikliklerin etkisini simüle etmek için oluşturulur.
Ulaştırma modeli, politika tedbirlerinin etkisini tahmin etmek ve bir SKUp’un geliştirilmesini desteklemek için yegâne yöntem olmak zorunda değildir. Alternatif, daha basit yöntemler, verilerin, zamanın ve kaynakların genellikle sınırlı olduğu küçük şehirlerde yaygın olan basit bağlamlar da gerçekçi seçeneklerdir.
Notes: Let's start with what the motivation is.
On the one hand, we have the growing complexity of travel patterns and the need to estimate changes in the behavior and mobility of individuals in response to new, also increasingly complex, transportation policies.
What this requires are more complex models or more sensitive to the variables for which we want to model their effects. And precisely the models are becoming more complex, they are increasingly disaggregated. This on the one hand, but on the other we have that there are more and more data sources that precisely allow these new models to be better calibrated and validated. So
And the models are moving towards explicitly modeling the activities in which the population participates throughout the day.
On the other hand we have new data sources.

## Slide 7
İnsan hareketliliği bir dizi seçim olarak değerlendirilebilir
İnsan hareketliliği, bir bireyin çeşitli faktörler ve kısıtlamaların bir unsuru olarak yaptığı bir dizi seçim olarak değerlendirilebilir.
Genel olarak, ulaşımla ilgili seçimler aşağıdaki gibidir:
İstikamet (bir faaliyete katılım)
Ulaşım modu seçimi
  Özel ulaşım sistemi
  Toplu taşıma sistemi
  Aktif hareketlilik (yürüme, bisiklete binme, vb.)
Güzergâh seçimi
Kalkış saati (varış saatine bağlı olarak)
Notes: Let's start with what the motivation is.
On the one hand, we have the growing complexity of travel patterns and the need to estimate changes in the behavior and mobility of individuals in response to new, also increasingly complex, transportation policies.
What this requires are more complex models or more sensitive to the variables for which we want to model their effects. And precisely the models are becoming more complex, they are increasingly disaggregated. This on the one hand, but on the other we have that there are more and more data sources that precisely allow these new models to be better calibrated and validated. So
And the models are moving towards explicitly modeling the activities in which the population participates throughout the day.
On the other hand we have new data sources.

## Slide 8
Modellerin sınıflandırılması (taksonomi)
Makroskobik modeller
Mikroskobik modeller
Ulusal/bölgesel/şehir modelleri.
Hareketlilik akışlar şeklinde modellenir.
Toplu ulaşım modelleri
Ayrıştırılmış modeller
Her bir davranış ağ içinde modellenir. Bir kavşağı, dönel kavşağı, yol şeridini vb. incelemek için tasarlanmıştır.
Karar alma süreci toplam kişi sayısına dayanır.
Karar alma süreci her birey için ayrıdır.
Notes: Let's start with what the motivation is.
On the one hand, we have the growing complexity of travel patterns and the need to estimate changes in the behavior and mobility of individuals in response to new, also increasingly complex, transportation policies.
What this requires are more complex models or more sensitive to the variables for which we want to model their effects. And precisely the models are becoming more complex, they are increasingly disaggregated. This on the one hand, but on the other we have that there are more and more data sources that precisely allow these new models to be better calibrated and validated. So
And the models are moving towards explicitly modeling the activities in which the population participates throughout the day.
On the other hand we have new data sources.

## Slide 9
Ulaşım modelleri haritası
Daha karmaşık modelleri seçmemize sebep olan bazı unsurlar:
Seyahat modellerinde karmaşıklık,
Ulaşım talebi politikalarında artan karmaşıklık,
Yeni veri kaynakları, nüfusun tutumuna dair büyük veriler (cep telefonları, GPS, sosyal ağlar...).
4 adımlı modelleme
Aktivite bazlı modelleme
Temsilci tabanlı modelleme
1950ler
1970ler
2000ler
Notes: Let's start with what the motivation is.
On the one hand, we have the growing complexity of travel patterns and the need to estimate changes in the behavior and mobility of individuals in response to new, also increasingly complex, transportation policies.
What this requires are more complex models or more sensitive to the variables for which we want to model their effects. And precisely the models are becoming more complex, they are increasingly disaggregated. This on the one hand, but on the other we have that there are more and more data sources that precisely allow these new models to be better calibrated and validated. So
And the models are moving towards explicitly modeling the activities in which the population participates throughout the day.
On the other hand we have new data sources.

## Slide 10
Model haritası
4 adımlı modelleme
Aktivite bazlı modelleme
Temsilci tabanlı modelleme
1950ler
1970ler
2000ler
Eklenen Modeller
Ayrıştırılmış Modeller
Bölgeler (TAZ, ulaşım bölgesi) arasındaki hareketlerin oluşumu ve çekiciliğine dayanır.
Bireylerin faaliyetlerini modeller ve bunları toplu olarak ağa bağlar.
Faaliyetleri ve ağ atamasını ayrıştırılmış bir şekilde modeller.
Notes: But what is the difference. The difference is at the level of aggregation. As I said, the 4-stage models, still widely used and useful, work at an aggregate level and model trips at the TAZ, transportation zone level. These models emerged in the 1960s in the United States, in Chicago, whose main objective was to evaluate the effects of new civil works, new roads, on traffic. So it made sense since it was evaluated how the level of service of the roads changed.
Then, in the 1970s, Faaliyet-Tabanlı Modelleme were formulated (although they have become popular in the last two decades), where the main idea is that the need to travel is a byproduct of the need to participate in activities. In general, these models evaluate in a disaggregated manner, at the individual and household level, the activities in which they participate, and then an assignment is made to the macroscopic network, aggregated in transportation zones.
This allows us to take into account the interdependencies between activities and, consequently, the decisions about mobility that individuals make, thus making a more realistic analysis of the responses of individuals to transportation policies. This is, for example, impacting the mode of transportation in the morning will impact the mode of transportation in the afternoon. The models are nothing new, they are based on econometric and discrete choice analysis.
Ben-Akiva et al. In the 1970s they proposed a practical framework for modeling mobility demand, opening the focus and basing it on the activities carried out by the population in the territory.
Why, because knowing what activities individuals participate in, the byproduct is obtained, which is the need to travel to carry them out, and, consequently, the mobility of the territory.
Finally, Ajan-Tabanlı Modelleme have appeared in the last two decades. They are still models based on activities but where the assignment to the network continues to be disaggregated, at the individual and agent level. Therefore, opening the door to a new paradigm where human behavior and their interaction with the territory can be modeled at a microscopic level.
Obviously, each one generates greater capabilities when evaluating more detailed actions in the territory, in the population or in the transportation network, but at a higher data and computational cost. Like everything, technology and capabilities are advancing and if some quite complex models are already being glimpsed, in the future we will surely be able to model mobility in real time.

## Slide 11
Geleneksel 4 adımlı model
Üretim/Çekim
Dağıtım
Türel dağılım
Ağ ataması
Bölgeye göre üretilen ve çekilen yolculukların elde edilmesi
Gelir
Taşıt Sahipliği
Aile büyüklüğü
Hane yapısı
Arazinin değeri
Konut yoğunluğu
Hane
İş
İş
Alışveriş
Üretim
Çekim
Çekim
Üretim
Çekim
Çekim
Üretim
Üretim
Çalışan Sayısı (x1)
Şekil 4.10 Gösterge değişkenli gerileme modeli
Hane başına HB yolculukları (Y)
2 veya daha fazla araç
1 araç
0 araç
Notes: Let's review the foundations of Geleneksel 4 aşamalı model since, for Faaliyet-Tabanlı Modelleme, the theoretical foundations are maintained, that is, similar models are used but trips are generated at the individual level.
The 4-stage model is based on the generation/attraction of trips by zone, the distribution of these trips between zones, the choice of transport mode and then the allocation of these trips to the network.
As you well know, generation/attraction is based on multiple linear models (econometric models) that, according to some socioeconomic characteristics, describe how many trips are generated and how many each area attracts.
The result is simply a travel table at an aggregate level, by zone. These econometric principles are maintained in Faaliyet-Tabanlı, Modelleme where the same socioeconomic variables model, for example, the number of tours that a given individual can take in a day, one or two, or the number of activities in which he or she participates on each tour. …

## Slide 12
Geleneksel 4 adımlı model
Üretim/Çekim
Dağıtım
Türel Dağılım
Ağ ataması
Bölgeler arasında bir maliyet işlevine göre oluşturulan ve çekilen yolculukların bölgeler arasındaki dağılımı.
Üstel İşlev
Güç işlev
Kombine işlev
Seyahat maliyeti (dakika)
Şekil 5.1 Farklı caydırıcılık işlevleri
Notes: Secondly we have the distribution of trips. Through a cost function measured, for example, in travel time, trips between areas are generally distributed with the gravity model. The result is an origin-destination matrix between zones of all mobility.

## Slide 13
Geleneksel 4 aşamalı model
Üretim/Çekim
Dağıtım
Türel Dağılım
Ağ ataması
Mevcut modların kullanışlılığının bir işlevi olarak bir başlangıç alanı ile bir varış alanı arasındaki yolculukların dağılımı (kesikli seçim modelleri, örneğin logit).
Mod seçimi başlangıçtan / varış noktasına /
Mod 1'i seçme olasılığı
Mod 2 ve 1 arasındaki fayda (maliyet) farkı
Maliyet 2 – Maliyet 1
Notes: The modal split is done with discrete choice models (generally multinomial logit or nested logit...) according to the usefulness of the available modes.
These discrete choice models are maintained in the Faaliyet-Tabanlı modelleme, but at the individual level, they are not applied at the aggregate level between zones.

## Slide 14
Geleneksel 4 adımlı model
Mod seçimi başlangıçtan / varış noktasına /
Ayrık seçim modelleri (örneğin logit), bir bireyin bir dizi alternatif arasından bir seçeneği seçme olasılığını belirtir.
Seçim modelleri, her bir kişi tarafından yapılan seçimi istatistiksel olarak kişinin nitelikleri ve kişi için mevcut olan alternatiflerin nitelikleri ile ilişkilendirir.
Tipik olarak seçimleri etkilediği düşünülen faktörler şunlardır:
Bireysel faktörler: Bireyin sosyo-ekonomik profili.
Diğer bireylerle ilişkiler: Bunlar ortak seyahatleri etkiler.
Arazi kullanımı: Kullanımların bir bölge üzerindeki coğrafi dağılımı.
Mevcut ulaşım sistemleri: Özel, kamu, aktif ya da paylaşımlı ulaşım sistemlerinin mevcudiyeti ve performansı.
Günün saati: Seyahat seçimleri, katılım faaliyetine gidiş ve varış gününün saatine göre değişir.
Ulaşım politikaları: Ulaşım politikaları bireyleri farklı şekilde etkileyebilir ve her bir bireyin belirli ulaşım sistemleri, modları veya güzergâhları üzerindeki maliyet algısını değiştirebilir.
Mod 1'i seçme olasılığı
Mod 2 ve 1 arasındaki fayda (maliyet) farkı
Notes: The modal split is done with discrete choice models (generally multinomial logit or nested logit...) according to the usefulness of the available modes.
These discrete choice models are maintained in the Faaliyet-Tabanlı modelleme, but at the individual level, they are not applied at the aggregate level between zones.

## Slide 15
Kullanıcı dengesi.
Üretim/Çekim
Dağıtım
Türel Dağılım
Ağ ataması
Geleneksel 4 adımlı model
Notes: Finally the assignment to the network, this is done by the program.

## Slide 16
Geleneksel modellemelerin bazı zayıf noktaları
Yolculuk temelli yaklaşımın bazı zayıf yönleri :
  Toplu hareketlilik kararlarının değerlendirilmesinde heterojen bir nüfus kümesinden oluşan analiz bölgeleri kullanılmaktadır.
  Hareketliliğin aktivitelere katılımdan kaynaklandığı kabul edilmemektedir.
  Yolculukların birbirinden bağımsız olarak modellenmesi: Ulaşım tercihlerini sınırlayan (ve bazen belirleyen) karmaşık mekânsal ve zamansal kısıtlamaların basitleştirilmesi.
Notes: Seeing this, therefore what are the weaknesses of traditional models. The 4-stage models generate travel ratios per person in each area, and you can generate as many matrices as you want. But then, they are added and the following decisions, where that demand goes and in what way, are made by zones, making the decisions as if that subset of the population were homogeneous.
Then we have the second point, Modeling trips independently of each other: simplifying the complex spatial and temporal constraints that delimit (and sometimes determine) the choice.
In reality there is an interrelation between the trips/stages you take in the afternoon and those you take in the morning. Also interpersonal relationships , that is, there are times where decisions are made at the household level, if someone takes the car, the rest of the family members will not be able to take it. Or then, for example, trips called escort, where one member accompanies another and then determines the pick-up, that is, the mobility of the family later.

## Slide 17
İnsan davranışının modellenmesinde karmaşıklık ve gerçekçilik
Shiftan & Ben-Akiva (2011)
Şekil 1 Seyahat talepleri modellerinde davranışsal gerçekçilik ve hesaplama karmaşıklığı
Dört Adım Tur Bazlı Aktivite Bazlı İdeal Davranışsal
Modeli Model Model Gerçekçilik
Davranışsal Gerçekçilik
Hesaplama Karmaşıklığı
Notes: In view of this, there is always the trade-off between complexity and cost.
A little reflection.
This figure conceptually shows how changing from travel-based models (4 stages) to more advanced models increases the realism with which human behavior is modeled but also the computational complexity. As the figure shows, the cost of model complexity increases exponentially but the marginal benefits of behavioral realism decrease.
We will see that in practice the cost of creating an Faaliyet-Tabanlı Modelleme has been decreasing over time and there are real cases where in a short time (2 years) we have gone from a 4-stage model to an ABM.
The following figure shows the same concept.

## Slide 18
Shiftan & Ben- Akiva (2011)
Aktivite Bazlı Modelleme aşağıdakilere duyarlı olmalıdır:
Talep yönetimi (otopark kısıtlamaları, trafik sıkışıklığı geçiş ücretleri...).
Arazi kullanımı
İnsan davranışının modellenmesinde karmaşıklık ve gerçekçilik
Toplam Model Avantajları
Şekil 2: Seyahat talebi modellerinde davranışsal gerçekçilik ve hesaplama basitliğinden sağlanan faydalar.
Davranışsal Gerçekçilik
Hesaplamalı Basitlik
Notes: Now here we have computational simplicity, where it gives us optimal modeling. But well, we will see that things are progressing and the administrations, which in the end are the ones who have the territory's models, should start betting on these models. We are dealing with complex but not complicated models; today there are many of these that have been in operation for years and are therefore validated.
Returning to the main motivations for the development of Faaliyet-Tabanlı modelleme, it is about providing a model that is sensitive to new policies. That is, we need a model as complex as the intervention we want to simulate is complex. That is to say something as silly as if I want to model the deployment of a network of bicycle paths that my model has the bicycle mode.
Therefore, while policy needs may vary from region to region, the minimum set of policies to which Faaliyet-Tabanlı modelleme should and can be sensitive are:
Demand management, including responses to different demand management strategies, such as parking restrictions and congestion pricing.
Land use policies that include mixed development, development concentrated in centers or corridors, and pedestrian-friendly site design.
Information and Communication Technology (ICT), and
Traffic Improvements.
Equity issues. For the model to be able to account for equity considerations, it must be able to plot outcomes for different subgroups of the population.

## Slide 19: Gündem
Saat | Başlık/Faaliyet
09:30-10:00 | Geliş ve Kayıt
10:00-10:05 | Gündemin ve Konu Başlıklarının Tanıtımı
10:05-10:50 | Temel Bilgilere Giriş: 4 Adımlı Modelleme
10:50-11:20 | Modern Yaklaşımlar: Faaliyete Dayalı Modelleme
11.20-11:30 | Ara
11:30-12:00 | Modern Yaklaşımlar: Temsilci Tabanlı Modelleme
12:00-12:30 | SKUp Bağlamında Mikro-Simülasyon
12:30-13:30 | Öğle yemeği
13:30-14:00 | Ulaşım Modellemesi Kullanarak SKUp Politikasının Değerlendirilmesi
14:00-14:45 | Ulaşım Modelleme Alıştırması
14:45-15:00 | Ara
15:00-15:50 | Yük Taşımacılığı Modellemesi
15:50-16:00 | Sorular ve Kapanış Konuşmaları

## Slide 20: Aktivite Bazlı Modelleme
Aktivite Bazlı Modellemenin Temel İlkeleri
Talep yönetimi analizi örneği
Kavramsal çerçeve
Aktivite Bazlı Modelleme Yaklaşımları
Ekonometrik yaklaşım
Ayrık seçim modelleri
Turlar (yolculuklar)
Günlük program (günlük planlama)
Planların ayarlanması
Özet: Temel Unsurlar
Davranışsal gerçekçiliğe geri dönüş

## Slide 21
Aktivite Bazlı Modellemenin Temel İlkeleri
Motivasyon, hareketlilik kararlarının bireyin katıldığı faaliyetlere dayanmasıdır. Yani, insanlar günlük bir zaman diliminde karmaşık karar verme modellerini takip ederek bazı faaliyetleri gerçekleştirmek için hareket ederler.
Aktivite Bazlı Modelleme, bireyleri ve ilgili bireylerin seçimlerini modellemektedir. İlk olarak, uzun vadeli seçimler simüle edilir (iş yeri, ev, taşıt sahipliği, toplu taşıma aboneliği...)
İkinci olarak ise günlük seçimler simüle edilir: aktiviteler, aktiviteleri birleştiren turlar, ulaşım modu, kalkış saati... Sonuç olarak ulaşım talebi türetilir.
Ben-Akiva and Bowman (1998)
İşveren tabanlı toplu taşıma teşvik programı
Sabah 7:30‘da tek başına araç kullanımı
Sabah 07.00’de
toplu taşıma
kullanımı
Sabah 06:00’da tek başına araç kullanımı
Notes: One of the most fundamental and well-known principles is that the demand for travel is derived from the demand for activity. This principle implies a decision framework in which travel decisions are components of a broader activity planning decision. Consequently, activity demand modeling is required.
Short- and long-term decisions are modeled.
Let's look at the example in the figure. It represents the daily activities and travel pattern of a person who used to drive alone to work at 7:30 a.m., went shopping along the way, and returned home at 4:40 p.m. This individual switched to public transportation in response to a company program that offers strong incentives for traveling by public transportation.
The change required me to start the trip earlier, at 7:00 am, to arrive on time. Because the store was not on the route, he decided to go straight home after work and go shopping later.
A pattern with two stops on a single tour was changed to a pattern with two single-purpose tours. In this case, a conventional trip-based model would likely fail to predict compensatory afternoon car trips.

## Slide 22
Talep yönetimi analizine örnek
Ben-Akiva and Bowman (1998)
İş yerinde özel araç kullanımının caydırılmasında geleneksel model (yolculuk bazlı) ile aktivite bazlı model (ABM) arasındaki farklar:
ABM gün boyunca gerçekleşen etkiyi ele alırken, geleneksel model sadece işe gidip gelme kısmına odaklanır.
Şekil 37.1 : (a) Politika analizine faaliyete dayalı yaklaşım: Politika müdahalesinden önce. (b) Politika analizine faaliyete dayalı yaklaşım: Politika müdahalesinden sonra.
Notes: Another very similar example. This figure illustrates the outcome of an intervention: a company-sponsored public transportation incentive combined with increased parking costs.
The change in activity pattern now requires three home-based tours (from home): trips to and from daycare in the morning, bus trips to and from work during morning and afternoon rush hours, and shopping by private vehicle in the late afternoon with a stop at the daycare on the way home.
A trip-based approach would probably reach the conclusion that rush hour trips are reduced, since it does not capture what we were talking about about the interdependencies between trips throughout the day.
However, an activity-based approach is more likely to conclude that the new policy was a mixed success due to the change in travel and activity patterns and the increase in car travel. An activity-based approach would capture the links between these events and suggest that transport policy change should be accompanied by other policies, such as incentives to take the child to daycare at work or close to home.

## Slide 23
Kavramsal çerçeve
Ben-Akiva and Bowman (1998)
Uzun bir zaman diliminde (yıllar) alınan kararlar.
Günlük zaman diliminde alınan kararlar
Kentsel kalkınma
Hanehalkı kararı
Hareketlilik ve Yaşam Tarzı (iş, ikamet, taşıt sahipliği, faaliyetler, vb.)
Aktivite ve Yolculuk Planlaması (sıra, konum, mod, vb.).
Uygulama ve Yeniden Planlama (rota, hız, otopark vb.).
Ulaşım sistemi performansı
Şekil 1.5 Aktivite ve yolculuk karar çerçevesi: Geniş bir zaman aralığında gerçekleşen birçok hanehalkı kararı birbirleriyle ve kentsel gelişim süreci ve ulaşım sistemi performansıyla etkileşim içerisindedir.
Notes: We have already seen the fundamental concept.
Let's now look at the basic framework of ABM.
This figure shows the broader framework where the Faaliyet-Tabanlı Modelleme is encompassed. It shows how activity planning decision making falls into a broader context, surrounded and connected to other relevant decisions.
For example, at a first level, decisions about the territory that the administration can make, housing, etc. They influence where people live and where they work. Governments can invest in infrastructure, provide services, and tax and regulate the behavior of people and businesses. Developers provide the locations for homes and businesses. So, where a company chooses to locate and its production decisions affect the job opportunities in that area and all of this affects how people move to work.
Therefore let's say that normally we can distinguish two levels. Long-term decisions and short-term decisions.
For each individual and household, decisions are made:
mobility and lifestyle decisions, which occur at long intervals of years. Whether to have one or two cars, the place of work, transportation subscriptions. For example, where we live and where we go to work can determine whether we have our own car or not.
Then we have the planning of activities and trips, taken in the short term and more frequently. If we are going to buy, if we are going somewhere, which family member does what activity, departure time...
Then, implementation and replanning: if we go on one route or another, if we go by bus or subway... Within the day, unplanned implementation and reprogramming decisions occur (for example route, departure time, travel speed, location parking, etc. (acceleration, lane change...).
In summary, urban development directly influences the decisions of individuals and households; Together, urban development and individual decisions affect transportation system performance, such as trip volume, congestion, and environmental impact. At the same time, the performance of the transportation system affects urban development and individual decisions.

## Slide 24
Kavramsal çerçeve
Aktivite Bazlı Modelleme
Genel olarak, Aktivite Bazlı modelin çıktısı; her bir yolculuğun kalkış saati, varış noktası ve modu hakkında ayrıntılı bilgi içeren bireyin aktivite ve yolculuk listesidir. Bu ayrıntılı çıktı, ağdaki eşleştirmeler için gerekli olan Başlangıç-Varış (OD) matrisleri hâlinde toplanır.
Aktivite Bazlı Modelleme için veri olarak birey ve hane başına sosyoekonomik bilgilere, arazi kullanımları ve ağ özellikleri hakkında bilgilere ihtiyaç vardır. Haritalama çıktıları ağ hizmet seviyesi (LOS) verileri sunar. Söz konusu veriler, Aktivite Bazlı modelin bir sonraki iterasyonunda girdi olarak kullanılır.
Bölgesel Ekonomi Modellemesi
Demografik Modelleme
Arazi Kullanım Modellemesi
Nüfus Sentez
Modellemesi
Yardımcı
Modelleme
Ağ Tedarik
Modellemesi
AQ Emisyon
Modellemesi
Notes: Let's look at another example, on a more practical level.

## Slide 25
İki Ekol
Standartlaştırılmış bir Aktivite Bazlı Model bulunmamaktadır. Bununla birlikte, aktivite modellemesine yönelik iki tür yaklaşım bulunmaktadır:
Ekonometrik yaklaşım (faydacılığa dayalı):
4 adımlı model ekonometrik modellere dayanmaktadır.
En yaygın yaklaşımdır (ABD'deki çoğu Aktivite Bazlı Modellemede kullanılır).
Birbiriyle ilişkili bir dizi ekonometrik denklemin yanı sıra mantıksal bir sırayla yapılandırılmış farklı seçim modellerine (çok terimli logit, iç içe logit...) dayanmaktadır.
Örnekler: ABD'deki modeller
Hibrit yaklaşım veya simülasyon:
Hibrit yaklaşım, olası kararlar kümesini iteratif bir şekilde (sezgisel) azaltan algoritmalarla ilgilenir. Bunlar insanın karar verme sürecini taklit etmeye çalışan yaklaşımlardır.
Örnekler: ALBATROSS (Arentze ve Timmermans, 2000), Hollanda'daki uygulama. TASHA (Roorda ve Miller, 2006), Toronto'daki uygulama.
Notes: In general, there is no single standard ABM. There are substantial differences between Activity Based Model systems.
Although in the end these are models that within the entire universe of combinations of activities, schedules, modes... result in the most feasible combination of activities for a given individual.
There is an important distinction, which distinguishes econometric models from hybrid simulation models.
Although as I say, both approaches try to "simulate" the decision-making of individuals in two stages: first the generation of sets of options (activities, tours, modes...) followed, sequentially or iteratively, by the final choice.
The classics are the econometric models. They focus on multidimensional choice based on utility, the typical discrete choice models, which are a system of equations that predict probabilities for each element to be chosen. It is the most implemented approach currently. However, nowadays, in utility-maximizing models there are some rules/restrictions that can nullify the econometric result, for example, if you have gone to drop off the child you have to pick it up again.
The hybrid approach, on the other hand, focuses most of its attention on generating sets of options, employing a complex search heuristic that produces a very small set of feasible options. In each iteration a simple choice model is used to select a feasible set. Until iteratively reaching the final set according to some rule.

## Slide 26
Ekonometrik yaklaşım
Ben-Akiva and Bowman (1998)
Tur
Günlük aktivite planı
Şekil 1.6 : Ekonometrik model sistemlerinin üç alt sınıfı, günlük program sonucunun alt bölümlere ayrılma biçimlerine göre tanımlanır. Yolculuk bazlı modeller programı tek yönlü yolculuklara ayırır. Tur bazlı modeller programı turlara ayırır. Günlük program modelleri ziyaretleri dolaysız olarak birbirine bağlar.
Notes: Within the class of econometric modeling systems, we identify three subclasses based on how each divides decision outcomes.
Currently, most work based on daily patterns where main and secondary tours are distinguished.

## Slide 27
Ayrık seçim modelleri
Her bir seçim seviyesinde, kişi her bir seçeneğin öngörülen yararını maksimize etmeye çalışır.
Daha düşük seviyedeki seçenekler, daha yüksek seviyelerdeki seçimlere tabidir.
National Academies of Sciences, Engineering, and Medicine. 2014. Activity-Based Travel Demand Models: A Primer. Washington, DC: The National Academies Press. https://doi.org/10.17226/22357.
Evet Hayır
Evet Hayır
Evet Hayır
Sahip Olunan Taşıt Sayısı
İş Yeri Konumu (TAZ#)
Toplu Taşıma Kartı Satın Alınması Gerekiyor Mu?
Alışveriş Yolculuklarının
Net Sayısı
Birincil Varış Noktasından Önce Durak Eklenmeli Mi?
Birincil Varış Noktasından Sonra Durak Eklenmeli Mi?
Yolculuğun Varış Noktası
Yolculuğun Başlangıç Saatleri
Ziyaretin Modu
Ziyaretin Sona Eriş Saatleri
Notes: First developed in the 1970s and 1980s in the Netherlands.
In the end we are faced with discrete choice models. Where at each level, the individual tries to maximize the expected utility of each option. Discrete choice models based on the principle of random utility maximization (RUM) have become the primary method for modeling activity and travel choices.
As we have been saying, the models we face are the location of the workplace (defined, for example, as TAZ), the number of cars per household that must be owned and whether a person would buy a public transport pass. The first is a choice at the household level and the second at the individual level.
Once we have this the individual has to make decisions about how they will move during the day. A key aspect of activity-based travel models is that trips are organized around tours. A tour is a series of trips that begin and end at your home or work anchorage location. By modeling decisions on the basis of a tour, consistency is imposed between the round-trip parts of the tour, so that the mode chosen to get to work determines the mode available for returning home.
Common to tour-based activity modeling is the identification of a main destination on each tour and the insertion of intermediate stops before or after the main destination. Additionally, there may be subtours within a tour. Then the individual first faces a choice model where he decides how many tours to take. Then for each tour and depending on the type (work tour, leisure tour...) how many stops will you make... Then, the mode. But all this always on the basis of usefulness given its characteristics.
Because many options are interdependent, it is recognized that what has been described as separate options, such as mode and destination, are actually bundled options, for example, choosing between combinations of mode and destination. Therefore, you can use nested logits or pass the utility in the form of a logsum of lower levels where the destination and mode of transport are jointly chosen.
Another example of a joint or conditional choice would be the choice of the start and end times of the tour, as shown in the figure. An obvious logical constraint is imposed here that the tour end time slots must be later than the tour start time slots. Implicit in this choice of start and end times is the duration of the tour. The choice hierarchy may seem incontrovertible due to the temporal ordering of start times before end times; however, the usefulness of the end time and duration may influence the start time of the tour.

## Slide 28
Turlar
Ben-Akiva and Bowman (1998)
İş
Araç Tahsisi
Mod
Şekil 1.9 Stokholm iç içe geçmiş logit iş ziyareti modeli. Hanehalkının işe katılımını, çalışanlar arasında otomobil tahsisini ve işe gidip gelme modunu koşullu bir hiyerarşi içinde temsil etmektedir.
Şekil 1.10 (a) Stockholm alışveriş ziyaretleri modeli. (b) Her bir alışveriş faaliyeti bir veya daha fazla hane üyesine atanır. (c) Bir alışveriş faaliyeti bir çalışana atanmışsa, ziyaret tipi modeli faaliyetin ev bazlı bir ziyarette mi, iş bazlı bir ziyarette mi yoksa iş ziyaretinde zincirleme olarak mı gerçekleşeceğini belirler.
Hareketlilik & Yaşam Tarzı
- Taşıt sahipliliği
- İş yeri konumu
Faaliyet ve Seyahat
İş Ziyaretleri
İş
Okul
Alışveriş
(2 tür)
Eğlence
(içeride)
Sosyal
(2 tür)
Kişisel İş (4)
Notes: Let's look at another example, the Stockholm model of the 90s I think.
For example, at the household level, it is chosen which individual uses the household's private vehicle and, if not, which mode he or she uses to go to work. That is, mobility and lifestyle choices affect work tours.
Given the work tours, shopping tours are chosen. You choose the frequency, who does it, whether it starts at home or at work, the mode and the destination.
The weakness of this is that the tours are modeled separately. There is a lack of a general pattern that connects the day's tours and includes the temporal dimensions in the structure of the model.

## Slide 29
Günlük Program veya Günlük Örüntü
Her bir turda verilen kararları kapsayan ve birleştiren bir günlük aktivite planındaki seçimleri temsil eder.
Günün saatine dair kararları içerir.
Her bir günlük plan, ana tur ve aktivite ile ikincil turlara bölünmüştür.
Model katlı terimli veya iç içe geçmiş logit sistemi olarak uygulanmaktadır.
Ben-Akiva and Bowman (1998)
Şekil 1.12. Günlük program sistemi prototipi. (a) Günlük örüntü, birincil ziyaret ve ikincil ziyaret, günlük faaliyet örüntüsü seçimini etkileyen beklenen ziyaret faydası ile bir hiyerarşi içinde modellenmiştir. (b) Günlük model 55 alternatifi ayırt eder.
Notes: Daily activity planning was first developed as a prototype for the greater Boston area.
Daily activity planning directly addresses the two weaknesses of tour-based models. First, it explicitly represents the choice of a daily activity pattern, which encompasses and unites the decisions of all tours. Second, it incorporates the time of day decision.
The concept remains the same, but daily planning is characterized by a choice of the main activity, the type of main tour and the number and purpose of secondary tours. The model distinguishes between the main tour of the day and secondary tours. For each tour, it models the destination, time of day and mode.
In the case of Boston, the model is implemented as a nested logit system, with tour decisions conditioned by the choice of daily activity pattern.
Tour utility also influences the choice of daily activity pattern through the expected utility mechanism.
This is a choice between 55 patterns that include
staying home all day or participating in activities that involve traveling, and
conditional on the trip, the choice of a particular pattern.

## Slide 30
Planların düzenlenmesi
Ekonometrik bir modelde ayarlama algoritması örneği. Örneğin, herhangi bir plan aşağıdaki kısıtlamaları karşılamalıdır:
Tüm aktiviteler saat sabah 0:00 ile gece 12:00 arasında başlamalıdır (evdeki son aktivite hariç).
Bir temsilci aynı anda yalnızca bir aktivite veya yolculuk gerçekleştirebilir.
Toplam yolculuk süresi X zaman dilimini aşmamalıdır.
Toplam aktivite süresi Y zaman dilimini aşmamalıdır.
Aktivite ve yolculuk bölümleri için harcanan toplam süre, Z = X + Y olmak üzere toplam Z saat dilimini aşmayacaktır.
Scherr et al. (2019)

## Slide 31
Özet: temel unsurlar
Her seviyede fayda temelli ayrık seçim modelleri kullanılmaktadır.
Genel olarak, günümüzde farklı aktivite turlarının oluşturduğu günlük aktivite planları kullanılmaktadır.
Ana aktiviteler, döngünün geri kalan aktivitelerini ve tur kararlarını belirler.
Hane halkı düzeyinde ortak kararlar da dahil edilebilir.
National Academies of Sciences, Engineering, and Medicine. 2014. Activity-Based Travel Demand Models: A Primer. Washington, DC: The National Academies Press. https://doi.org/10.17226/22357.
Notes: In the left column, "Tour and Trip Details" are shown divided into several different subcomponents.
The main destination, mode choice and planning models are displayed in a box,
While the models for generating intermediate stops and location are different,
Finally, the choice of mode per stage and choice of departure time remain at the last level. You see that the mode is chosen twice. This is useful because within a tour, for example, you can go to work by public transport and then walk to eat, for example.
This general sequence of modeling the different types of options is followed in virtually all practical Faaliyet-Tabanlı Modellemeing systems in the United States.
In many Faaliyet-Tabanlı Modellemeing systems, the day's activity patterns are predicted separately for each individual in the household, predicting the number of tours each person takes in the day for each activity purpose (and possibly some other aspects of the full-day pattern as well, depending on the system design of the specific model). Leaving the influence of the other members of the home as exogenous.
The right column indicates that there is a second class of models that do include explicit simulation of interactions within the home. Such models contain additional subcomponents in the daily schedule portion that first predict the types of plans at the household level and then predict joint travel activities and tours involving multiple household members, and use those predictions to condition the plans on individual level.
The daily activity pattern of ABMs is where model system designs vary most widely in practice. However, regardless of the exact sequence and specification of the options being simulated, the main result is the exact number of tours each individual takes for each of the different activities and tour purposes. Often, purposes are grouped into three different types according to priority: mandatory activities (work, studies), maintenance activities (medical, shopping...) and recreational activities.

## Slide 32
Davranışsal gerçekçiliğe geri dönüş
Karmaşıklığa karşı davranışsal gerçekçilik
Arazi kullanımı ve nüfus projeksiyonu
Nüfus üreteci
Hane halkı & bireyler
Taşıt sahipliliği
Ağ performansı
Ev & iş yeri konumu
Aktivite Bazlı Seçim Modelleri
Günlük aktivite & yolculuk örüntüleri
Park seçimi
Rota seçimi
Atama
Birleştirilmiş
Dağıtılmış
Şekil 3. Birleştirilmiş ve ayrıştırılmış model sistemi.
Notes: For Activity Based Model to have the desired behavioral realism, they must be theoretically sound and of sufficient resolution to explain policy impacts.
An Faaliyet-Tabanlı Modelleme should predict activity participation and sequencing over time, explicitly taking into account spatial, temporal and social constraints, while taking into account interdependence between individuals in a household and between trips. .
Faaliyet-Tabanlı modelleme should be integrated with lower-level decisions, such as parking options or route choice, and higher-level decisions, such as residential location, work location, and car ownership. That is, ABM is not understood if it is not in conjunction with other models.
The solid arrows show the current practice of most Faaliyet-Tabanlı modelleme. The dashed arrows show the additional integration required with higher-level decisions, such as land use and private vehicle ownership, and with lower-level decisions, such as parking and route choice. If not, these are given as exogenous input.
From the bottom level, most current Faaliyet-Tabanlı modelleme have done little to account for the effect of route choice and the effects of that behavior on activity participation, duration, and scheduling patterns. Most models use traditional aggregate allocation models rather than utilizing all the benefits of Faaliyet-Tabanlı modelleme.
In balancing practicality and behavioral realism, the emphasis should be on specific policy aspects of interest.
In the Tel-Aviv model, great emphasis was placed on parking supply and pricing and congestion pricing. Consequently, detailed time-of-day and parking models were developed. A special parking supply, cost and availability model was also developed for San Francisco. They also expanded their ABM to model teleworking.
At Southern Michigan they expanded their model to go to half-hour resolution for activity participation.
With all this in mind, one may feel overwhelmed by the level of data needed to calibrate these models. This is partly true, but traditionally, this data is collected from the same surveys as for traditional models.
Nowadays, with geolocation technologies (integrated in mobile phones) the door opens to combine them to generate more precise models.
Of course, there are uncertainties generated by the model and the input data, but the good thing is that we have the theoretical and practical framework ready to receive all this information.

## Slide 33: Aktivite Bazlı Modellemede Belirsizlik
Belirsizliğin kaynakları
Tel-Aviv modeli
Singapur modeli

## Slide 34
Belirsizliğin kaynakları
Literatürün çoğu geleneksel modellere odaklanmaktadır. Genellikle ilk üç adımda (yolculuk üretimi/çekimi, yolculuk dağılımı ve mod seçimi) ortalama belirsizliğin arttığı, son atama adımının ise ortalama belirsizliği azalttığı söylenmektedir.
Genel olarak, sonuçların toplanma düzeyi (VKT(Taşıt başına yolculuk edilen km), VHT (taşıtın yaptığı yolculuk süresi), kişi başına ziyaret...) ve yineleme sayısı göz önüne alındığında, sonuçlar kararlı değerlere yakınsamaktadır.
Genel olarak, nüfus segmenti ne kadar spesifik olursa belirsizlik de o kadar artar.
Girdideki, model parametrelerindeki, seçilen örneklemdeki ve simülasyondaki belirsizlik arasında bir ayrım yapılabilir.
Girdi Veri
Parametreler
Örneklem
Simülasyon
Notes: With increasing complexity, uncertainty analysis becomes more important and becomes a non-trivial procedure.
Population sampling is often used in disaggregated model runs to shorten model run time. For example, ABM can be applied to 10% of randomly chosen individuals, and the resulting demand matrices formed are multiplied by 10. For different sample sizes, some studies report that from a 30% sample of in the population, changes as significant as 10 to 30%, for example, are not observed. This can be explained by the fact that the size of the sampling error is proportional to the inverse of the square root of the sample size.
Parameter uncertainty originates from calibrated parameters and the use of their estimates instead of actual values. Some transportation authors call parameter uncertainty 'sample uncertainty' (e.g. [3]) since the error in calibrated parameters is due to using a sample instead of the population. The order of magnitude of parameter uncertainty for traditional models varies between 4% and 7% for the total travel demand of different modes and between 4% and 5% for the traffic volume of different links. .
Simulation error is probably one of the most explored sources of uncertainty in model specification in the case of ABM.
The allocation method, which could be included within the simulation error, used in the model system is another uncertainty factor. This element of uncertainty is well known in the literature. We will see an example where the error derived from the tour generator is studied, in Tel-Aviv.
In general, simulation errors for some models are reported to be negligible or below 1% when model results are averaged over 10 or more runs. Some specific submodels of a complex model required a much larger number of runs to stabilize the results, with 100 or more runs.

## Slide 35
Örnek: Tel-Aviv Aktivite Bazlı Model (ABM)
Bölge (1500 km2) 1219 trafik analiz bölgesine (TAZ) ve 3.3 milyonluk bir nüfusa bölünmüştür.
1996'da yapılan İsrail Ulusal Yolculuk Alışkanlıkları Anketi (NTHS) modelin geliştirilmesi için ana veri kaynağıdır. Bir ana tur ve bir ikincil tur modellenmiştir.
Tel Aviv ABM deneyimi, belirsizlik kaynaklarının kapsamlı bir analizine ihtiyaç olduğunu ortaya koymuştur. Bunun önemi, proje değerlendirmesi için Aktivite Bazlı Model kullanımının nihayetinde senaryoların karşılaştırılmasına (örneğin, "projeler eklenmiş" ve "projeler eklenmemiş") dayanması ve alternatif senaryolar için model sonuçları arasındaki farkın herhangi bir rastgele bileşeninin kontrol edilmesi gerektiği gerçeğiyle ilgilidir.

## Slide 36
Tel-Aviv modelinin unsurları, logit modelleri hiyerarşisine dayanmaktadır:
Hane başına özel araç mevcudiyeti.
Bir kişinin ana aktivitesi. Ev dışındaki aktiviteler için model, ana aktivitenin varış yerini ve yolculuğun ana modunu belirler.
Zaman aralığı: çıkış yerinden kalkış ve ana varış yerinden kalkış saatlerinin ortak seçimi, 15 uygulanabilir seçim alternatifi vardır.
Bölge düzeyinde varış noktası, 1219 bölgeden oluşan tam setin kullanılması.
Ana mod seçimi.
Ara durak seçimi, ziyarete bir durak eklenmesinin neden olduğu ek faydasızlığı dikkate alarak durağın varış yerini de belirler.
Örnek: Tel-Aviv Aktivite Bazlı Model (ABM)
Notes: The Tel Aviv ABM system comprises a hierarchy of logit and nested logit models for the main tour stop, i.e. activity type, time of day, destination and mode. The intermediate stops are then modeled conditionally to the main stop models. The Tel-Aviv model accounts for up to two tours for each person: the most important tour of the day, called the main tour, and the second most important tour of the day, or the secondary tour.
At the highest level, the private vehicle availability model predicts the probability of the number of cars available to the household.
Following this model, the main activity model determines a person's main activity. Alternatives include work, education, shopping, other types of activities outside the home, and staying home. For activities outside the home, the model determines the destination of the main activity and the main mode of the tour.
Destination choice models are estimated using the full set of 1219 traffic analysis zones as alternatives.
In terms of time, 5 time periods are included as follows: early morning (MO) from 03:00 to 06:30, peak morning (AM) from 06:30 to 08:30, midday ( MD) from 8:30 a.m. to 3:00 p.m., afternoon peak (PM) from 3:00 p.m. to 8:00 p.m., and evening/evening (EV), from 8:00 p.m. to 3:00 a.m.
Because time period models predict the joint choice of departure times from the origin and primary destination, there are 15 feasible choice alternatives.
Later models determine whether there is an intermediate stop on the way from home to the main destination and/or from the main destination back home.
For each intermediate stop, the model determines the stop destination taking into account the additional disutility caused by adding a stop to the tour. Once all the details of the main tour, which includes the main activity of the day, are determined, the model estimates whether there is an additional secondary tour for which a similar set of models is estimated.
The results of these models are translated into OD trip matrices that are assigned to the network.

## Slide 37
Tel-Aviv modelinin yapısı:
Bireylerin listesi.
Yolculuk Oluşturucu (önceki slayt): Bireylere göre turların ve yolculukların listesi.
Gezi listelerinin BV matrislerinde toplanması.
Ağa atama.
Ulaşım ağı hizmet seviyesinin güncellenmesi ve yolculukların yeniden oluşturulması.
Örnek: Tel-Aviv Aktivite Bazlı Model (ABM)
Notes: Population generation produces a list of individuals, which represents the population of the study area for a given year and for a given sampling rate. This can be the entire population or a random sample which is often used to shorten execution times.
The Trip Generator applies the AMB to each person included in the generated population sample. As a result, a description of the daily trips of each person is obtained (explained above). As input, the network service level is needed. Such as time in the vehicle, walking time, waiting time, number of transfers, etc.
The tours are then divided into individual trips that are summarized in mode-specific demand matrices for different periods of the day. These arrays are then used as input for mapping, which performs all necessary traffic and car mappings. The current version of the model uses static traffic allocation.
Tours are regenerated and then assignments are remade with newly obtained demand. The loop is repeated several times to eliminate the influence of the initial demand. In summary, it converges to an equilibrium where aggregate outputs are stable.

## Slide 38
Tur üreticisindeki belirsizlik
Tur üreticisindeki rastgelelik.
Bütünleştirilmiş düzeyde, simüle edilen yer değiştirme sayısında çok fazla değişkenlik yoktur (şekil).
Bununla birlikte hücre düzeyinde, daha sonra stabilize olmasına rağmen çok fazla değişkenlik vardır. Örneğin, belirli bir iterasyonda bazı değerlere sahip 117.000 hücre bir sonraki iterasyonda boş hale gelir. Bir sonraki iterasyonda, bir yolculuk verisine sahip 93.000 hücre bir önceki iterasyonda boş olmayan hücrelerdi.
Notes: However, there is randomness related to tour generation and this is the central source of uncertainty in ABM.
The metric that will be used in this work for the uncertainty analysis is the vehicle-hours traveled (VHT). They investigate the automobile demand matrix for the AM period.
In this image it is seen that the aggregate distribution of trips in the matrix is quite stable. However, there are considerable changes at the cell level.
At a given iteration of the model run, the number of non-empty cells is about 270,000, of which about 150,000 cells (55%) contain a trip. In the next iteration, about 117,000 non-empty cells (42%) are transformed into empty cells, of them 93,000 (34% non-empty cells or 80% transformed non-empty cells) were cells with a trip in the previous iteration. Similarly, there are changes in the opposite direction: about 117,000 empty cells are transformed into non-empty cells in the next iteration.
This “flip-flop” situation throughout the iterations is quite stable, which this aggregate indicator does not show.

## Slide 39
Tur üreticisindeki belirsizlik
Burada şu soru ortaya çıkmaktadır: Talep matrisindeki rastgelelik, model sonuçlarındaki rastgeleliğe nasıl dönüşmektedir?
Bir önceki iterasyona kıyasla belirli bir BV’deki seyahat süresi arasındaki farkın dağılımı
İterasyonlar boyunca ortalama seyahat süresinden sapma
Notes: To analyze the uncertainty, the vehicle-hours for each origin-destination in tomorrow's rush hour are considered. The figure on the left shows the distributions of the time differences of each OD, for various iterations of the model run. The differences are calculated between successive iterations between the same cells.
????The average difference varies in the range [-0.19, 0.15] and the standard deviation varies in the range [0.16, 0.25]. Since the average OD time in the matrix (not weighted by demand) is about 41 minutes, the corresponding CV of the time differences is about 0.007, which is significantly lower compared to the car demand matrix. There are two reasons that can explain this low CV: first, the known high smoothing power of the assignment procedure, which is related to its aggregative nature: trips of around 270,000 cells (OD pairs) are assigned to the network with around 10,000 links, of which many are interdependent. Second, in ABM, the LOS values calculated from the allocation results in one iteration affect the formation of the demand matrix for the next iteration. Therefore, the randomness of the demand is not completely “white” and this also has an impact on the low value of CV.????
->Statistical tests applied to the VHT values show that the values are random with 95% confidence. This is seen in the figure to the right.
This means that after several iterations of a model, the value of vehicle-hours stabilizes, with a standard deviation of around 420 vehicle-hours. An important consequence can be derived here: the model loop [LOS->Tour Generator>Demand Matrices->LOS] considerably suppresses the random component, otherwise the deviation from the average VHT would have grown with the iterations, since In each iteration more uncertainty would be added. This consequence is quite natural: for example, if the service level deteriorates for some OD pair, then the probability of performing an activity for this OD pair will decrease, which will consequently reduce the number of trips for this OD pair, and vice versa. .
However, the standard deviation of VHT obtained above is usually not acceptable for practical purposes. For example, small or medium-sized network interventions can generate VHT savings of 100 to 200 vehicle-hours, so random error in the model results will not allow a correct evaluation of the project. Therefore, measures must be taken to stabilize the model results. Consequently, averaging methods are used.

## Slide 40
Ortalama yöntemleri
"MSA-R" yöntemi, birkaç başlangıç iterasyonundan sonra, atama sonuçlarının rastgeleliğinin stabilize olduğu gerçeğine dayanmaktadır. Bu nedenle, modelin her iterasyonundan sonra elde edilen sonuçların ardışık olarak ortalaması alınabilir.

## Slide 41
Ortalama yöntemleri
"MSA_M" yöntemi, her iterasyondan sonra talep matrislerinin ortalamasının alınmasına dayanmaktadır. Talep matrisleri yüksek değişkenlik gösterir ve bu da sonuçta model sonuçlarının rastgeleliğini etkiler. Talep matrislerinin ortalamasının alınması matrisin hücrelerindeki değerleri yumuşatacak ve dolayısıyla modelin stabilliğini artıracaktır.

## Slide 42
Ortalama yöntemleri
Bir iterasyon yapıldıktan ve hizmet seviyesi (LOS) matrisleri elde edildikten sonra, tur üreticisi aynı nüfus ve hizmet seviyesi kullanılarak birkaç kez etkinleştirilir ve elde edilen talep matrislerinin her seferinde ortalaması alınır. Daha sonra atamalar yapılır ve bir sonraki iterasyon için yeni hizmet seviyesi matrisleri elde edilir.
Notes: The “Quasi-aggregation” method is a similarity to aggregate modeling. After doing one iteration of the model run and obtaining the LOS matrices, the TG is activated several times using the same population and the same LOS, and the obtained demand matrices are averaged each time. The assignments are then made and new LOS matrices are obtained for the next iteration. The method is called “Quasi-aggregation” since asymptotically, when the number of TG (inner loop) activations increases, the averaged demand matrices will represent the probability distributions of OD trips, just as in the aggregate models. Of course, an unrealistically large number of internal iterations would be required to achieve good approximation of the probability distributions, however, smoothing the demand matrices will have a positive effect and skipping assignments after each internal iteration will save execution time.

## Slide 43
Ortalama yöntemleri
Genel olarak sonuç, hesaplama açısından da benzerdir.
Notes: Despite the differences mentioned above, it can be seen that the efficiency of all procedures is quite similar, and none of them can be preferred based on the available statistical data. More detailed analysis is required to refine the resulting conclusion.
Ideally, the model standard deviation should not exceed 100-150 VHT so that fine resolution policies aiming to reduce, for example, 200 VHT can be considered statistically significant.

## Slide 44
Singapur SimMobilite
SimMobilite modelinin uzun, orta ve kısa vadeli olmak üzere üç bileşeni vardır. Orta vadede ABM yer almaktadır:
22 alt model
4 tür aktivite
9 ulaşım modu
Her biri yaklaşık 35.000 kişiden oluşan bir örneklem ile hareketlilik anketleri (HITS-2008, 2012 ve 2016) ile kalibre edilmiştir.
Notes: Let's look at another example with the Singapore model.
The ABM model predicts the pattern of activities throughout the day and was developed and calibrated using a variety of data sets from Singapore. The results showed that the order of magnitude of all types of uncertainty considered depends largely on the frequency with which the alternative is predicted in the choice process.
It contains three simulators: Long term [20], Medium term [21] and Short term [22]. The model built in SimMobility is open source. It covers the modeling of millions of agents, from pedestrians to drivers, traffic lights to bus and train operations, from second-by-second to year-by-year simulations.
The activity model (called Preday model within SimMobility) is the generator of daily activities. The medium-term simulator predicts daily trips at the household and individual level. The study that we will see only analyzes the uncertainty of the model that generates the activities, the Pre-day.
The Preday model consists of 22 discrete choice submodels that follow a nested, multinomial logit structure. The figure on the right shows its structure in which different discrete choice models are linked and consists of three levels: daily activity pattern, tour and intermediate stop.
The Preday model is developed for four different types of activities: work, education, shopping and others. Home, work, and education locations are not modeled, as they are explicitly modeled at the long-term level. In destination/location choice models, zones (TAZ) are used. Nine different modes are modeled within Preday, which are: MRT, Bus, Private Bus, Solo Car, Car with 2 Passengers, Car with 3 Passengers, Motorcycle, Taxi and Walking.
From the mode choice and mode-destination models, accessibility in the form of individual-based log sums for each activity type is then transferred back to models at the day pattern level, helping to capture the effects second order (in terms of selecting changes in daily patterns). These logarithmic sums represent the maximum utility of a set of alternatives from a set of options in a discrete choice model consistent with random utility theory.
Tour-level time-of-day models are jointly predicted with arrival and departure times in 30-minute time steps.
Finally, the Pre-day models (ABM) have been estimated primarily using data from the Mobility Survey (HITS)-2008, 2012 and 2016, each containing data from more than 35,000 people. These data were collected through stratified random sampling from various spatial segments of Singapore. Additionally, along with the geographic strata, the type of housing is also used as a variable to define strata during the data collection phase.
These data sets were used to validate the model results and adjust some model parameters to adjust for relevant changes. Along with the HITS data, land use and network data (such as travel times and travel costs for public and private vehicles) for different time periods of the day were also incorporated for model calibration.

## Slide 45
Modeldeki belirsizlik
En etkili parametreler filtrelenir.
Parametreleri örneklemek için simülasyonlar.
Model parametrelerindeki, seçilen örneklemdeki ve simülasyondaki belirsizlik incelenmiştir.

## Slide 46
Parametrelerdeki belirsizlik
Ön taramanın ardından 654 parametreden oluşan bir örnekleme gerçekleştirilmiştir.
Ardından, standart yanılmaları kullanarak ve korelasyonlarını koruyarak normal bir dağılım varsayan her parametreden bir Latin Hiperküp Örneği kullanılarak 500 simülasyon gerçekleştirilmiştir. Ardından, her bir parametrenin esnekliklerini değerlendirmek için metamodeller (her bir alt model için) oluşturulmuştur.
Nihai parametreler için varyasyon katsayıları hesaplanır (standart sapma/ortalama).
Notes: A single calibration allows obtaining data on parameter estimates, their standard errors and correlations. Therefore, parametric sampling can be applied from a multivariate normal distribution with mean values equal to the parameter estimates and standard deviations equal to the standard errors, maintaining correlations.
For screening,
First, the number of parameters was reduced by excluding all constants from the utility functions used in the choice submodels of the Preday model.
Second, sensitivity tests were performed for each of the submodels separately to filter out more parameters.
Then, from these distributions of the parameters, a Latin hypercube sampling is done (it is like a Monte Carlo)
Linear regression (log-log was used) is a metamodel that provides the elasticities and can be applied if the linear relationships are statistically robust. If the regression coefficients are standardized, it represents the relative contribution of each variable to the overall variance of the output.
Elasticities are then derived and a selection of less sensitive variables is made.

## Slide 47
Parametrelerdeki belirsizlik
Görüldüğü üzere, farklı sonuç değişkenleri için varyasyon katsayıları %3 ile %49 arasında değişmektedir. Değişkenlik, daha nadir olan model seçimleri veya model sonuçları için daha yüksektir. Ayrıca sentetik nüfusun daha küçük sosyo-demografik kesimleri için de daha yüksektir.
Notes: As can be seen, the coefficients of variation for different outcome variables vary between 3% and 49%. The variability is greater for model options or model outcomes, which are rarer. It is also higher for smaller sociodemographic segments of the synthetic population. For example, the number of people taking at least one tour per day is very high (1.5 million people) and therefore the related parameter uncertainty of 5.6% is relatively small.
On the contrary, the number of people who take two tours per day is relatively small (about 55.6 thousand), so the coefficient of variation related to the uncertainty of the parameter is 39%. However, this is not always true. For example, the walking mode share is smaller than the private bus mode share (4% vs. 11%, respectively) and has lower variability (4% vs. 7%, respectively).
This can be explained by the different composition of the submodels and the variability of their parameters that affect the outcome variables of the Preday model, and also by the number of corresponding respondents in the survey used as a sample.

## Slide 48
Örnekteki belirsizlik
Araştırmacılar, hesaplama zamanından tasarruf ve örnekleme hatasının iyi bir kombinasyonunu sağlayan örneklem büyüklüğünün %30 olduğunu iddia etmektedir.
Notes: To speed up the execution of a Preday model when the model is applied, the result is calculated only for a 10% random sample of the synthetic population and then the results are multiplied by ten.
This simplification in the model result was tested by making samples of different sizes: 5%, 10%, 20%, 30% and 50%.
As one would expect, the size of the sampling error is proportional to the inverse of the square root of the sample size. The size of the sampling error for each output also depends on the frequency with which an alternative is selected.
For example, for the alternative with the number of tours equal to 1, which is very frequent, the coefficient of variation is less than 1% for a sample size of 10%. In contrast, the number of work-based sub-tours is very small (they represent 9500 trips for the entire synthetic population of around 4 million people).
In general, the graphs show that the elbow of the curve is reached around 30%, that is, 30% is the sample size that provides a good combination of saved calculation time and sampling error. Although for the variables that represent the frequent alternatives, the corresponding coefficients of variation do not exceed 1% even for a sample size of 10%. These findings are similar and in line with all previous studies that analyzed the variation of results for different options or market segments for sampling uncertainty.

## Slide 49
Simülasyon belirsizliği
Örnekler ve parametreler sabit tutulmuş ve Gün Öncesi modelinin 100 simülasyonu gerçekleştirilmiştir.
Bu durumda varyasyon katsayısı genellikle düşüktür.
Tablo 10
Ziyaret sayısı ve işe dayalı alt turlar için simülasyon belirsizliğini temsil eden ortalamalar, standart sapmalar ve varyasyon katsayıları.
Tablo 12
Ziyaret modeli payları için simülasyon belirsizliğini temsil eden ortalama standart sapmalar ve varyasyon katsayıları (tüm faaliyetler için).
Notes: Simulation error in ABM models is an error due to assigning an option to each individual in the synthetic population (or a subsample thereof) based on the calculated probability.
The simulation uncertainty for the Preday model was based on 10% random samples of the entire population, in all simulations to ignore the sampling error (presented in the previous subsection) for this test.
One hundred simulations were run for the Preday model for the same 10% sample and the results were multiplied by 10 to obtain the total population.
Like sampling uncertainty, simulation uncertainty depends on how often a particular alternative is chosen. For example, for the number of people with 0, 1 or 2 tours per day, the simulation uncertainty does not exceed 2%, which is very low, while for the number of work-based sub-tours it is quite high for all modes (between 6.6% and 42% depending on the mode).
The reason for this is a smaller original survey sample for such tours and, as a result, less stable results in terms of variation of the explanatory variables. According to the authors, these results give sufficient reason to believe that if an ABM model is integrated with traffic simulation, the impacts of simulation and sampling uncertainties on link volumes and travel times will also be lower.

## Slide 50
Model belirsizliğine ilişkin sonuçlar
Hataların büyüklük sırası büyük ölçüde alternatifin tahmin edilme sıklığına bağlıdır.
Modelin tahmini parametreleri en büyük belirsizlik kaynağıdır (örnekleme ve simülasyondan daha fazla) ve bunların büyüklük sırası örneklemin büyüklüğüne bağlıdır (bu durumda, hareketlilik anketleri).
Tablo 14
Seçilen değişkenler için simülasyon belirsizliğini, örnekleme ve parametre belirsizliğini temsil eden varyasyon katsayıları
Notes: Table 14 provides the general summary of the order of magnitude of the types of uncertainty analyzed in this study for three important model results: the number of people taking 1 trip per day, the number of trips with an intermediate stop per day, the modal fee for driving alone. It is clearly evident that the parameter uncertainty is significantly higher compared to the model specification uncertainties.
The results showed that the order of magnitude of sampling and simulation errors largely depends on the frequency with which the alternative is predicted in the choice process.
In the case of uncertainty related to the estimated parameters of the model, its order of magnitude depends on the size of the sample, the data sampling mechanism used for the estimation, and the way in which the parameters are estimated with the method of maximum likelihood.
The results showed that the coefficients of variation for different outcome variables of interest vary between 3% and 49%.
Therefore, parameter and input uncertainties are what lead to greater variations in the results. The uncertainty calculated for the model results in this study will allow practitioners to choose a strategy to handle it. This could include, for example, measures aimed at reducing uncertainty (i.e. a larger population sample when running simulations and a larger sample of household travel surveys) or designing transport policies/interventions that are tailored to the possible results within the calculated uncertainty range.
Uncertainty analysis studies conducted for a four-step model (e.g., Zhao and Kockelman [15]) showed that the final input and parameter uncertainty can be attenuated if the demand side is integrated with the traffic assignment. Some studies suggest that this attenuation could occur due to capacity constraints, which restrict the variability of link flows and the fact that link flows are the sum of variable flows between DO pairs (and that the coefficient of variation of a sum is less than or equal to the sum of the coefficients of variation of each component).

## Slide 51: Uygulamanın durumu
ActivitySIM (& PopulationSIM)
Ticari yazılım

## Slide 52
ActivitySIM
ActivitySIM, Metropolitan Planlama Kuruluşları Birliği tarafından yönetilen bir ortaklıktır.
Amaç, işbirliği yoluyla, ölçeklenebilir aktivite bazlı modelleri için bir platform oluşturmaktır.
Hedef, geliştirme ve bakım maliyetlerinin yanı sıra yeni ulaşım otoriteleri için uygulama maliyetlerini azaltmaktır.
ActivitySIM hane başına ve birey başına turları kalibre eder ve oluşturur. Ağa atama başka bir yazılımda yapılır.
ActivitySIM Python tabanlıdır.
Modüler bir tasarımla geliştirmeyi kolaylaştırır.
Notes: Historically, in the United States, the use of Faaliyet-Tabanlı modelleme has been deployed by consultancies that have reused the same models in different regions. Let's say that the new regions have benefited from a “donor” model and the model has been recalibrated for the specific region. Then, it was refined or as new needs arose, functionalities were incorporated in a modular way.
This is the idea behind ActivitySIM. From the development of models based on activities in San Francisco, Oregon, San Diego, etc. It has been released open source so that any person/organization can use it.
The objective is, through collaboration, to generate a model of activities that scales over time.
Because as we have said before, as you increase the complexity of the model, you increase the implementation costs and resources and this is usually the main barrier to adopting this type of models.
So, whether you like it or not, there are common elements that can be reused for other regions and just calibrating them is enough.
So the benefit is double. First, you already have a model made (the algorithms) and you can benefit from the calibration of a donor “donor” model, what you have to do is recalibrate it with your mobility surveys or other data sources. I think the one that is public is the one in San Francisco, the one in Atlanta and SemCog.
On the other hand, you benefit from new modules that new organizations develop, now we will see an example.
AcitivtySIM calibrates and generates the tours per household and per individual. The assignment to the network is done in other software.

## Slide 53
Aktivite bazlı model için tüm nüfusa ihtiyaç vardır.
Genel olarak hareketlilik anketleri, hanehalkı ve birey bazında sosyoekonomik verilerin yanı sıra aktivitelere katılımı (4 aşamalı modellerle aynı anketler) elde etmek için kullanılır.
Genellikle bir bölgenin marjinal dağılımlarına uyan sentetik bir nüfus oluşturulur.
PopulationSIM, ActivitySIM'de yer alan açık kaynaklı bir sentetik nüfus üreticisidir.
Amerika Birleşik Devletleri'ndeki uygulama durumu, TAZ ulaşım bölgelerinden çok daha yüksek çözünürlükte Mikro Ulaşım Bölgeleri (MAZ) kullanmaktır.
Maricopa modeli, MAZ başına ortalama 195 birey yoğunluğu. Link
PopulationSIM
Notes: PopulationSim requires a population sample (also called a seed or reference sample) and marginal distributions (also called controls or targets). Population samples can come from the census public use microdata sample or mobility survey data. Marginal distributions can be specified at multiple geographic levels.

## Slide 54
SEMCOG (Güney Doğu Michigan)
SEMCOG örneği: 2 yıl içinde 4 aşamalı bir modelden sıfırdan bir Aktivite Bazlı Model oluşturmak.
Pratik açıdan bazı ilgili sonuçlar:
Ne tür verilere ihtiyaç vardır? Çoğunlukla 4 aşamalı model için anketler ve arazi kullanımları ile toplananlarla tutarlı. Okul kayıtlarını da dahil etmeleri gerekiyordu.
Ayrıca, GPS kayıtları ve toplu taşıma araçlarında yapılan anketleri içeren bir alt örneklemleri vardı.
Sentetik nüfus için nüfus sayımı verileri.
Uyarı: geleneksel modellerde (yolculuk bazlı) her bölgede ikamet edenler için yolculuklar ve ikamet etmeyenler için yolculuklar vardır. ABM gerçekten yerleşik olan bireylerin yolculuklarına odaklandığından, yerleşik olmayanların modellenmesi sağlanmalıdır. Sonunda tüm talep segmentleri eklenir.
ActivitySIM iş parçalarından oluşmuştur, bu nedenle ne kadar çok RAM'e sahip olursanız, hesaplama süresi o kadar kısa olur.
ActivitySIM platformunda toplu taşımanın otomatik kalibrasyonunun yanı sıra görselleştirici faaliyetler de bulunmaktadır.
https://github.com/SEMCOG/SEMCOG_ActSim

## Slide 55
SEMCOG (Güney Doğu Michigan)
Başlangıç noktası olarak MTC (San Francisco) modeli kullanılarak yapılan küçük kalibrasyon sonuçları.
Notes: From here we see the potential of using a donor model.

## Slide 56
SEMCOG (Güney Doğu Michigan)
Zorunlu Yer Seçimi
Taşıt Sahipliliği
Kişi Türüne Göre Toplam Ziyaret Oranı
Notes: The transferability of an ABM was first investigated for the ALBATROSS model for two municipalities (Voorhout and Apeldoorn) in the Netherlands. The results were satisfactory except for the choice of transportation mode.
In the United States, it has been a very common practice as virtually every major metropolitan region has an Faaliyet-Tabanlı Modelleme.
The CT-RAMP ABM that was developed for the mid-Ohayo region was then transferred to Lake Tahoe.
In [103] the transferability of the DaySim model system developed for Sacramento to four regions in California and two other regions in Florida was investigated. The results show that the activity generation and scheduling models can be transferred better than the mode and location choice models.
The Dallas Fort Worth (DFW) model was transferred to the Southern California region [104].
Outside the US
The TASHA model system developed for Toronto was transferred to London [105], and another study [106] also evaluated the transferability of TASHA to the context of the island of Montreal.
In general, empirically, it is said that the result will be potentially good if an ABM is transferred within the same state and/or in regions with similar densities.
However, perfect transferability is not easy to achieve due to different policies and planning needs, as well as the size of regions and data availability... Although some tests appear to have worked reasonably, it is equally important to evaluate how much accuracy is important in transferring models and what is the best way and from where to transfer the models.

## Slide 57
VISUM & ABM
Visum, Python (Visum COM) aracılığıyla ABM’nin entegrasyonuna izin verir
Harici açık kaynak çözümleri, örneğin PopGen
İlk etapta, standart veri yapılarını uygulayacağız ve mevcut yerleşik Visum işlevselliği tarafından kapsanmayan işlemler için komut dosyası tabanlı bir prototip sunacağız. Talep, atama için toplanır, ancak bireysel yollar kişilere rastgele atanacaktır.
Kullanıcı tarafından geliştirilen script
Operasyon
Kullanıcı tarafından geliştirilen ABM
Kullanıcı tarafından geliştirilen script
Atanmış Turlar & Geziler

## Slide 58
VISUM & İsviçre Demiryolu Şirketi SBB
İş birliği ABM’yi anlamak, veri yapılarını geliştirmek, daha verimli işlemek ve çıktıları görselleştirmek için yapılmıştır.

## Slide 59
VISUM & İsviçre Demiryolu Şirketi SBB
Bireylerin, yolculukların ve turların izlenebilirliği ve analizi için yeni yapılar geliştirilmiştir.

## Slide 60
Yapı
Ticari yazılımlar hızlı hesaplama süreleri sunmayı amaçlamaktadır.
ABM'de hesaplama süresi bölge sayısı ile değil nüfus büyüklüğü ile belirlenir.
Notes: Now they are working on improving computing times. Because in ABM you have to work with large matrices. The computational time is not given by the number of zones but by the size of the population. Swiss example 8.6 million people and 8000 areas. I think the computing time was less than 24 hours, but it depends a lot on the RAM.

## Slide 61
Yapı
Seçim Modeli Listesi
"TourFreqW" seçim modelinin özellikleri
Notes: As we saw in ActivitySIM, the models are presented in table form.
Each choice model has a subtable for its specification.

## Slide 62
İşlem sonrası

## Slide 63
İşlem sonrası
Ulaşımla ilgili eylemlerin analizi.
Yeni köprüyü kullanan insanlar nerede yaşıyor? Ve yer değiştirmenin amacı nedir?
Notes: In the end, what the software focuses on is post-processing, which is efficient and visual. It is so important then, once everything is calibrated, to be able to squeeze out the level of disaggregation that the ABM provides.
Then, for example, we could say, oh boy, we're going to put a congestion toll on this type of travel.

## Slide 64
İşlem sonrası
Notes: The same thing here, you can see the profile of the reason for travel of the people who pass over the bridge.

## Slide 65: Gündem
Saat | Başlık / Faaliyet
09:30-10:00 | Geliş ve Kayıt
10:00-10:05 | Gündemin ve Konu Başlıklarının Tanıtımı
10:05-10:50 | Temel Bilgilere Giriş: 4 Adımlı Modelleme
10:50-11:20 | Modern Yaklaşımlar: Faaliyete Dayalı Modelleme
11.20-11:30 | Ara
11:30-12:00 | Modern Yaklaşımlar: Temsilci Tabanlı Modelleme
12:00-12:30 | SKUp Bağlamında Mikro-Simülasyon
12:30-13:30 | Öğle yemeği
13:30-14:00 | Ulaşım Modellemesi Kullanarak SKUp Politikasının Değerlendirilmesi
14:00-14:45 | Ulaşım Modelleme Alıştırması
14:45-15:00 | Ara
15:00-15:50 | Yük Taşımacılığı Modellemesi
15:50-16:00 | Sorular ve Kapanış Konuşmaları

## Slide 66: Temsilci Tabanlı Modelleme
MATSim : Çok Temsilcili Ulaşım Simülatörü

## Slide 67
MATSim
Trafiğin mikro ölçekli modellemesi: MATSim, ortaya çıkan trafik akışlarının ve ürettikleri tıkanıklığın integral mikro ölçekli simülasyonunu gerçekleştirir.
Talebin mikro ölçekli davranışsal modellemesi/Temsilci-Tabanlı Modelleme: MATSim, günlük programı ve sentetik yolcuların kararlarını izleyerek talebin mikroskobik bir tanımını kullanır. Geçmişe bakıldığında, bu "temsilci tabanlı" olarak adlandırılabilir.
Karmaşık uyarlanabilir sistemler/eş-evrimsel algoritmalar: MATSim, tüm güne ait yolculuk programının deneyimlenen faydalarını, birlikte evrimsel tarama yoluyla ortaya denge veya kararlı duruma getirmek üzere optimize eder.
MATSim tek bir günü modellemek için tasarlanmıştır.
Bireylerin yolculuk programının kullanımıyla ABM
Ağ atama
Kişi başına günlük kâr (amaç fonksiyonu)
Ağdaki planı veya simülasyonu birey başına optimize eden evrimsel algoritma.
Notes: Matsim is an open source, created by the ETH University of Zurich and the TU of Berlin.
It is a microsimulation model of mobility behavior and activities.
MAT Sim is based on the co-evolutionary principle. It's as if it were a genetic algorithm. Each agent repeatedly optimizes their daily activity plan while. Each individual must have one or more possible plans and in each iteration it is optimized in a meta-heuristic manner. All based on an objective function, which is still utility.
http://ci.matsim.org:8080/job/MATSim-Book/ws/partOne-latest.pdf
The modification of the plan is made according to each individual's rating of their chosen plan and four dimensions are considered:
departure time (and, implicitly, duration of the activity) (Balmer et al., 2005),
route (Lefebvre and Balmer, 2007),
mode (Grether et al., 2009) and
destination (Horni et al., 2009, 2012).
Eventually, an equilibrium is reached, subject to constraints, where agents cannot further improve their plans unilaterally.
Replanning offers different strategies to adapt plans, ranging from random mutations to approximate suggestions, to best response responses where, in each iteration, the current optimal option is searched. For example, routing is often a best response modification, while time and mode replanning are random mutations.

## Slide 68
İlk talep
MATSim birey başına bir dizi faaliyet planı ile başlar. Bu, hane halkı anketlerinden veya nüfus sentezleyicilerinden gelebilir.
İlk nüfus, aktivite planı, modu ve bitiş zamanı ile tanımlanır.
Sonraki iterasyonlarda, hareketlilik simülatörü rotalar ekler ve bitiş zamanlarını değiştirir ve puanlama modülü her planı puanlar.
Değiştirilebilen unsurlar
Notes: The initial demand is a population, each with its activity plan or possible activity plans.
As we have already seen, the input data are usually mobility surveys, synthesizers, mobile phone data with additional work to extract modes and types of activity or other synthetic generation.
MAT Sim has modules for route choice, mode choice, (departure) time choice and secondary activity location choice and consequently everything else must be provided exogenously. This refers, in particular, to the sequence of activities of each person. As we saw with ActivitySIM this does not provide you with long-term decisions such as number of vehicles per household, etc...

## Slide 69
Hareketlilik simülatörü
Kuyruk(lanma) simülasyonu. “İkili kum saati”.
Araçlar kuyruğun sonuna gelene kadar serbest hızla ilerler
Kuyruk, bağlantının akış kapasitesine karşılık gelen varış sırasına göre hizmet eder (trafik ışığı).
Bağlantı dolu olabilir (geri dökülme)
Notes: Once we have each individual with their plans, they are simulated in a mesoscopic simulation on the network using queuing simulation. This allows efficient simulation of very large regions without needing to reach the microscopic level.
Each link is modeled as a queue. First in first out. Each link has capacity characteristics (how many vehicles it can fit) and travel time characteristics, like typical macroscopic BPR functions.
A car entering a link from an intersection is added to the end of the waiting queue. It remains there until the travel time of the link with free flow elapses and until it is at the head of the waiting queue and until the next link allows entry, so spillback or gridlock effects can be modeled since each link has a capacity attribute.
The mesoscopic approach explicitly models time and sets an individual to a specific link at a specific instant. So you can go to an almost instantaneous resolution of where each individual is. It is not like a macrosimulation where the vehicle is simultaneously on all the links that make up its route.
This allows the microscopic analysis of car-following to be omitted and reduces the computational cost. That for modeling large regions is already fine.

## Slide 70
Puanlama ve yeniden planlama
Simülasyon gerçekleştirildikten sonra, her bir temsilci kendi planını (fayda) puanlar: bir aktiviteyi gerçekleştirmek için pozitif fayda ve yolculuk yapmak, beklemek veya geç varmak için negatif fayda.
Her aktivitenin bir marjinal fayda fonksiyonu vardır (Charypar ve Nagel, 2005; Vickrey, 1969; ve Arnott ve ark.1993 modeline dayanmaktadır)
Şekil 5-3: Puanlama fonksiyonunun gösterimi. ÜST: Faaliyetlerin ve ayakların bireysel katkıları. ALT: Bir gün boyunca puan birikimi.
Notes: Each individual agent learns by maintaining multiple plans, which are scored (with econometric utility), selected based on the score, and sometimes modified.
An individual can
change your plan,
change the activity time, or some activity
change the route.
For some agents, a plan is copied, modified (according to some rule or as if it were a genetic algorithm where there is some random component), and then selected for the next iteration.
For agents who already maintain a plan, depending on their score, you can replan, change the activity time, change the route or mode.
Each module is given a weight, determining the probability by which one strategy or another is taken. As seen in the end, the utilities of each individual converge to stable values.

## Slide 71
Temsilci Tabanlı Modelleme
Temsilci Tabanlı Modelleme, ulaştırma alanındaki politika önlemlerine daha da duyarlıdır:
Zaman bağımlılığı (geçiş ücretleri, kalkış saati, açılış saati değişiklikleri, soğuk çalıştırma emisyonları, ...)«
“Katı kısıtlamalar” (bir gün 24 saattir, ailelerdeki araçlar/taşıt paylaşımı sınırlıdır...)
Yeni hareketlilik: elektrikli araçların indirme profilleri, otonom araçlar, talep üzerine hareketlilik...
Eşitlik analizi (bireylerin sosyo-ekonomik koşullarına göre)
https://www.matsim.org/gallery/paris
Notes: By maintaining the information in both the ABM and the allocation, it is possible to trace how a certain policy affects or goes to very specific segments of the population.

## Slide 72: Temsilci-Tabanlı modelleme örnekleri
Yeni Kapasiteler
Polonya'da Elektrikli Taksiler
Hollanda'da sıfır emisyon bölgelerinin etkilerini analiz etmek için kentsel mal taşımacılığına yönelik ampirik bir çoklu-temsilci modelinin uygulanması
Talep üzerine otomatik hareketliliğin etkilerinin temsilci tabanlı simülasyon yoluyla değerlendirilmesi: Singapur üzerine bir çalışma
Aktivite Bazlı Modellemenin temsilci tabanlı simülasyonu ve cep telefonu verilerini birleştirerek COVID-19 ile ilgili müdahalelerin kentsel ortamlardaki etkilerini tahmin etmek

## Slide 73
Yeni Kapasiteler
ABM’nin analiz kapsamı
Türel değişimi teşvik etmek için stratejiler.
Zirve saatlerinin esnekleştirilmesi.
Talebin azaltılması/modifikasyonu.
Fiyatlandırma (ücretli yollar New York, San Francisco)
Eşitlik (marjinalleştirilmiş grupla üzerindeki etki...)
Aktif hareketlilik
Yeni hareketlilik anlayışları (otonom, elektrikli, paylaşımlı, mikromobilite...)
Notes: Let's do a review. As we have seen, the new capabilities that ABM entails are:
The evaluation of modal change strategies.
The evaluation of making departure time more flexible.
Reduction in travel demand.
Pricing. Congestion tolls require understanding how people will respond to tolls. They can also analyze what side effects they have. Faaliyet-Tabanlı modelleme have already been used in this capacity in regions such as New York City and San Francisco to study area- and cordon-based tolling and pricing, respectively.
Equity. ABM produces results that can be used to measure the impact of policies on populations of interest, including historically marginalized groups.
Active mobility. Faaliyet-Tabanlı modelleme can represent space (and short trips) at a more detailed scale than traditional models. This distinction is increasingly important as micromobility services grow in many cities and regions.
Moving on to agent based, they allow the traceability of the variables that influence mobility (for example, charging of electric vehicles) and model autonomous behaviors, such as when to recharge or the modeling of on-demand services.

## Slide 74
Polonya'da Elektrikli Taksiler
MATSim kullanılarak Polonya’nın bir şehrinde taksi filosunun elektrifikasyonunun değerlendirilmesi.
Mevcut talep, elektrikli bir taksi filosuyla karşılanabilir.
Bischoff, J., & Maciejewski, M. (2014). Elektrikli taksi filolarının temsilci-tabanlı simülasyonu. Transportation Research Procedia, 4, 191-198. https://doi.org/10.1016/j.trpro.2014.11.015
Şekil 1. Elektrikli taksi filosunun gün içindeki şarj durumu; çizgi filo genelini göstermektedir: maksimum (mavi) minimum (yeşil) ve ortalama (kırmızı).
Notes: Regarding the latter, let's look at an example with the electrification of the taxi fleet in Poland. The objective is to benefit from agent simulation to be able to trace the battery status of each taxi.
According to the simulation in normal operations, the fleet can cover the current demand without increasing the waiting time of taxi users in any case.

## Slide 75
Polonya'da Elektrikli Taksiler
Taksilere olan talebin belirli zirve noktaları vardır (büyük etkinlikler, kötü hava koşulları veya toplu taşımadaki kesintiler sırasında...) ve bu nedenle talebin karşılanıp karşılanamayacağını bilmek ilgi çekicidir.
Mevcut yüzde yedilik artış, hem yakıtla çalışan bir filo hem de elektrikli bir filo için hala yönetilebilir düzeydedir. Daha fazla bir artış, elektrikli filo için ortalama bekleme sürelerinde çok daha dik bir artışa neden olacaktır.
Şekil 2. Artan genel taksi talebi altında bir taksi için ortalama bekleme süresi; çizgiler yakıtla çalışan (yeşil) ve BEV (kırmızı) filoları için ortalama bekleme sürelerini göstermektedir.
Notes: Now, the demand for taxis has certain peaks that can endanger the quality of the service, and what they are dealing with here is a kind of sensitivity analysis.

## Slide 76
Polonya'da Elektrikli Taksiler
Elektrikli şarj altyapısının boyutlandırılması, elektrikli taksi filosuna ve uyguladıkları şarj kısıtlamalarına göre optimize edilebilir.
Şekil 2. Mevcut şarj sayısına bağlı olarak seçilen bir taksi durağındaki şarj cihazı doluluğu.
Notes: The cost-effective use of BEVs also depends on the number of chargers required for stable operations. Therefore, for the aforementioned everyday scenario, the number of chargers was reduced to five, two and finally one per taxi stop. The latter is equivalent to one charger for every ten vehicles. If a taxi requires charging while the charger is busy, it will queue until the charger is available. A reduction to five and two chargers does not influence the simulation result from either the passengers' or drivers' perspective, but it dramatically reduces the amount of charging energy used at peak times and therefore the charging energy. necessary network (Fig. 3). Even with just one charger per queue, the average wait time for customers remains the same, although taxis dispatch slightly differently to requests than with 10 chargers per queue. This reduction results in slightly different request-to-taxi assignments, however, the average wait time for taxis remains the same.

## Slide 77
Polonya'da Elektrikli Taksiler
Taksilerin ilk gelene ilk hizmet esası yerine en yüksek SOC'ye (şarj durumu) göre dağıtılması muhtemelen daha verimli hizmet sağlayabilir. Bu, özellikle akülerin tam güçle şarj edilemediği kış aylarında geçerli olabilir.
Ortalama bekleme süresi yarım dakika azalır ancak bazı araçların geliri artırılır.
Şekil 4. Sevkiyat algoritmasına bağlı olarak gelir kilometresi. SOC hareketleri ile sevkiyat, mutlak minimum azalırken aynı zamanda medyanı artırır.
Notes: Taxis generally leave taxi ranks on a first-come, first-served basis (FIFO). What they propose is dispatching them rather by the highest battery charge level (SOC) could possibly produce a more efficient service. This could be especially relevant during the winter, when batteries cannot be charged to full power.
In this case, the waiting time is reduced by half a minute. At the same time, however, the overall average mileage per vehicle increases slightly from 272 to 273 km.
Another result is that some vehicles receive significantly more requests than others and, therefore, the income from taxi trips is less distributed. See
Another example of the potential of ABM.

## Slide 78
Hollanda'da sıfır emisyon bölgelerinin etkilerini analiz etmek için kentsel yük taşımacılığına yönelik ampirik bir çok temsilcili modelin uygulanması
Bu çalışmanın alanı Hollanda'nın en yoğun bölgesidir ve mallar için güçlü bir üretim ve çekim düğümü olan Rotterdam Limanı'nı içermektedir.
Amaç, Rotterdam'ın merkezinde düşük emisyonlu bir bölgenin etkisini incelemektir.
de Bok, M., Tavasszy, L., & Thoen, S. (2020). Hollanda'da sıfır emisyon bölgelerinin etkilerini analiz etmek için kentsel mal taşımacılığı için ampirik bir çok aracılı modelin uygulanması. Ulaştırma Politikası. https://doi.org/10.1016/j.tranpol.2020.07.010
Şekil 2. Çalışma alanı: Hollanda'nın Güney Hollanda eyaleti
Notes: Let's now look at a multi-agent model for merchandise distribution. The trick here is to be able to discriminate between the different types of cargo and the different types of actors who will have a very different impact depending on the type of cargo. But they are models that have not been applied to practice.
They have the potential to simulate the impacts on logistics decision making and the heterogeneity of agents in freight demand:, and in this way these models are more suitable to account for the heterogeneity in logistics decision making.
Instead of simulating activities, they simulate shipments by company or by logistics node.
This area is the most urbanized region in the Netherlands and has a population of 3.3 million and 1.8 million jobs. In addition, it also contains the most important seaport in Western Europe, the Port of Rotterdam.

## Slide 79
Hollanda'da sıfır emisyon bölgelerinin etkilerini analiz etmek için kentsel yük taşımacılığına yönelik ampirik bir çok aracılı modelin uygulanması
Model şunlardan oluşmaktadır:
Sevkiyat Sentezleyici: Firmalar veya lojistik düğümler arasında yük türüne ve sevkiyatın brüt ağırlığına göre bireysel sevkiyatlar.
Tur oluşumu: Araç tipi seçimi, tur oluşumu ve günün saati.
Ağ ataması
Üretim
sevkiyat boyutu
Araç türü
Tüketim
Şekil 1. MASS-GT'de lojistik seçimler için kavramsal model
Notes: The empirical basis for this is provided by an exceptionally large data set of truck trip diaries in the Netherlands. The database includes information about the vehicle, the route and the shipments that were made, and has a high data density. The survey is digitalized and is mandatory in the Netherlands for those trucks registered in the database. This data source is essential for the calibration of logistical choice behavior.
The model consists of three modules: a shipping synthesizer, a tour training model, and mapping.
Shipping Synthesizer . The result is a set of all shipments to and from sender and recipients and/or logistics nodes in the study area.
Contains the type of merchandise and the gross weight of the shipment, and the attributes of the sending and receiving companies
The starting point is an aggregate cargo demand matrix, which is first divided into different types of distribution channels (direct shipping or through a logistics operator). Then it is derived by market shares with a MonteCarlo simulation until the final tables are found.
Tour training . The second module simulates the selection of vehicle type, tour formation and departure time.
The model is based on a logit.
First, the decision to add a shipment to the tour and, second, choosing the type of shipment to add.
Restrictions such as vehicle capacity, duration of the journey (i.e. maximum work shift), type of shipment are taken into account.
The utility function includes transportation costs, types of goods, type of vehicle, and type of location.
-------
For example, it is observed that shipments to and from multimodal terminals (e.g., ports) are transported on direct routes, while routes that begin at a distribution center tend to have more stops, which the model can capture. These logistical choice models allow us to simulate the impact of changes in distribution channels on tactical choices in route formation. We will analyze this in the case study with urban consolidation centers.

## Slide 80
Hollanda'da sıfır emisyon bölgelerinin etkilerini analiz etmek için kentsel yük taşımacılığına yönelik ampirik bir çok aracılı modelin uygulanması
Lojistik operatörü tarafından oluşturulan ziyaretlere örnek
Taşıma bölgesi düzeyinde tahmin edilen ve gözlemlenen yük (brüt yük ağırlığına göre.)

## Slide 81
Hollanda'da sıfır emisyon bölgelerinin etkilerini analiz etmek için kentsel yük taşımacılığına yönelik ampirik bir çok aracılı modelin uygulanması
Kentsel Konsolidasyon Merkezleri (UCC) ile Sıfır Emisyon Bölgesinin (ZEZ) Etkileri.
UCC'lerin etkisi göz ardı edilemez: ZEZ içindeki emisyonlar azalır (çünkü tüm ulaşım sıfır emisyonlu araçlarla gerçekleşir) ancak ZEZ dışındaki araç kilometrelerinde bir artış görebiliriz.
Notes: In the zero-emissions zone, it is mandatory that all shipments be distributed or collected through the consolidation center. Only ZE vehicles are allowed in the city center and we consider ZE vehicles to have a marginal share in the existing fleet.

## Slide 82
Hollanda'da sıfır emisyon bölgelerinin etkilerini analiz etmek için kentsel yük taşımacılığına yönelik ampirik bir çok aracılı modelin uygulanması
Tablo 2
ZEZ'e ve ZEZ'den taşınan sevkiyatların lojistik göstergeleri.
Tarım ürünleri ve canlı hayvanlar
Gıda maddeleri ve hayvan yemi
Katı mineral yakıt
Petrol ürünleri
Cevherler ve metal atıkları
Metal ürün
Mineraller ve inşaat ürünler
Gübreler
kimyasallar
Mamul ve muhtelif eşyalar
Boş araç
Toplam
Notes: The result is not trivial, but has several elements.
On the one hand, shipments are consolidated and redirected, which improves logistics efficiency.
However, on the other hand, an increase in total vehicle-km is observed, due to routing due to having to go to consolidation centers.
Policy makers can use these detailed simulations to optimize the location of planned consolidation centers to minimize additional VKT or see exactly why this increase in VKM is occurring.

## Slide 83
Talep üzerine otomatik hareketliliğin etkilerinin değerlendirilmesi
temsilci tabanlı simülasyon: Singapur üzerine bir çalışma
Amaç: Singapur'da Talep Üzerine Sürücüsüz Hareketliliğin (AMOD) etkisini incelemek.
AMOD filo operasyonları modellenmiştir (taleplerin araçlara atanması ve filonun yeniden dengelenmesi dahil) ve bunlar çok modlu bir mezoskopik trafik simülatörüne entegre edilmiştir.
Sonuçlar, AMOD'un düzensiz bir şekilde uygulanmasının ağ tıkanıklığında ve araç-km'de önemli artışlara neden olabileceğini göstermektedir.
Oh, S., Seshadri, R., Azevedo, C. L., Kumar, N., Basak, K., & Ben-Akiva, M. (2020). Talep üzerine otomatik hareketliliğin etkilerinin temsilci tabanlı simülasyon yoluyla değerlendirilmesi: Singapur üzerine bir çalışma. Transportation Research Part A: Policy and Practice, 138, 367-388. https://doi.org/10.1016/j.tra.2020.06.004
Ortalama bekleme süresi AMOD
Notes: Let's look at another example. In this case it is the Singapore model, the one we have seen before on the topic of uncertainty. The objective is to study the impact of autonomous vehicles on demand in Singapore.
For one thing, autonomous vehicles have the potential to alleviate congestion by increasing ride-sharing and reducing car ownership, and to complement public transportation.
On the contrary, AMOD can, in fact, worsen congestion due to induced demand, what they call “the cannibalization of public transport” (that is eating into its market share, and an increase in vehicle kilometers traveled (VKT) due to empty travel.
On the demand side, they use an ABM, which is based on data from a smartphone-based stated preference survey conducted in Singapore.
On the supply side, this is why using an Ajan-Tabanlı Modelleme makes sense. To model the operations of the AMOD fleet, it is necessary that, despite the redundancy, the agents are autonomous. That is, they can make decisions at any time, that is, whether to pick up a user or not, change routes, rebalancing operations (go to an area with more demand), etc. That is why it is necessary to reach the micro level.
The study results suggest that an unregulated introduction of AMOD can cause significant increases in network congestion and VKT, and has important policy implications that could inform future AMOD implementations.

## Slide 84
Talep üzerine otomatik hareketliliğin etkilerinin değerlendirilmesi
temsilci tabanlı simülasyon: Singapur üzerine bir çalışma
AMOD (SMS kontrolörü) modelinin dahil edilmesi
Notes: Let's go back to the Singapore model and see where the change is. SimMobility is made up of three main components that operate on different time scales.
The long-term (year-to-year) model captures land use and economic activity. It predicts the evolution of land use and property, determines the associated life cycle decisions of agents, and accounts for interactions between individuals and companies.
The Mid-term (day-to-day) simulator models the daily transport supply and demand of passengers and goods: it simulates the behavior of agents, their activity and travel plans, and the movement of vehicles at a mesoscopic level. .
Within the Mid-Term we have the Pre-day module, which is actually the system that generates activities and tours, the ABM. It is organized into three levels: daily activities, the tour and intermediate stops (which are multinomial logit models).
The main activities are education, work, shopping and others.
Secondary activities are intermediate stops within a particular tour, as seen in the figure.
The final result is travel agendas with a resolution of 30 min, the destination at the zonal level and the travel mode for each trip/tour, including the assignment of requests to vehicles and rebalancing.
In the Within-day module, you choose the route, the choice of departure time...
Here is the change. Let's say that the within-day module, in a normal model, could be translated as introducing train schedules exogenously. Give them as fixed. What the offer module does is establish the public transport offer dynamically. So, this module includes bus and train controllers to manage public transportation operations.
Then, an on-demand mobility services controller (SMS controller hereinafter) has been integrated into the offering module that models all aspects of the on-demand services (including MOD, AMOD). What I have mentioned before.

## Slide 85
Talep üzerine otomatik hareketliliğin etkilerinin değerlendirilmesi
temsilci tabanlı simülasyon: Singapur üzerine bir çalışma
Akıllı hareketlilik kontrolörü (MOD ve AMOD)
Notes: The concept of the controller is shown in this figure.
The passenger sends a request to an on-demand service, specifying the pickup point and destination.
The controller receives requests continuously, periodically processes these requests and assigns vehicles to them. Additionally, the controller performs "rebalancing" actions for idle vehicles, which could involve directing them to a parking lot or navigating to a specific area (such as a high-demand area).
The actions of the SMS controller are transmitted to the service vehicles in the form of updates to their agendas. Assigning requests to vehicles is done using a simple heuristic. To maximize ride-sharing, the controller attempts to match ride-sharing requests to vehicles that are already serving one or more requests and then to idle vehicles.
This involves iterating through each of these vehicles and finding the first vehicle that can satisfy the request while meeting certain constraints on the waiting time and travel time of both the incoming request and the other requests the vehicle already has. vehicle.

## Slide 86
Talep üzerine otomatik hareketliliğin etkilerinin değerlendirilmesi
temsilci tabanlı simülasyon: Singapur üzerine bir çalışma
Senaryolar:
AMOD, toplu taşımada ağa giriş/ağdan çıkış yolculukları ve kapıdan kapıya yolculuklar için hizmet vermektedir.
Fiyatlandırma mevcut taksi ücretlerine göre değişmektedir (taksi ücretlerinin %75, %100 veya %125’i).
Belirtilen Tercihler anketine göre AMOD yüksek benimseme senaryosu.
AMOD orta düzeyde benimsenme senaryosu MOD'un mevcut payına eşittir.
AMOD filosunu yoğun saatlerdeki kullanım oranına ve düşük bekleme sürelerine göre optimize ederler.
Notes: For each scenario, they determine an optimal fleet size, such that they try to guarantee that utilization is close to 100% during peak hours, that the service rate of requests is close to 100% and that waiting times are close to 100%. low enough.
Once we have this, we focus on 2 adoption scenarios and 3 pricing scenarios.

## Slide 87
Talep üzerine otomatik hareketliliğin etkilerinin değerlendirilmesi
temsilci tabanlı simülasyon: Singapur üzerine bir çalışma
Yüksek ve ılımlı benimseme senaryoları ve oranları için model değişimi, taksilerin %75'i kadardır.
Sonuç olarak, toplu taşımadaki «yerini alma halinin» altı çizilmektedir.
Notes: What is shown here is what the specific modal change has been. It is clear what they said about the cannibalization of public transportation. And if you look down here you can see PT (AMOD) there really is a fine line from car to PT AMOD. That is to say, a modal change has not been promoted by facilitating access to public transport.

## Slide 88
Temel senaryoya kıyasla araç-km'de yüksek artış. Önemli bir kısmı (yaklaşık %20) boş seferlerden kaynaklanmaktadır (AMOD_OP).
Talep üzerine otomatik hareketliliğin etkilerinin değerlendirilmesi
temsilci tabanlı simülasyon: Singapur üzerine bir çalışma
Notes: Consequently, high increase in vehicle-km compared to the base scenario.
All this despite the fact that AMODs are directly sent to the nearest parking lot upon completing a trip. However, it must be taken into account that displacements in AMOD depend on the operations algorithms and therefore could be improved in the model and reduce the increase in vehicle-km.

## Slide 89
Simülasyon aynı zamanda etkinin sürekli bir zamansal boyutta görülmesini de sağlamaktadır.
AMOD'un devreye girmesi sadece yoğun saatlerde seyahat süresini artırmakla kalmayıp aynı zamanda tıkanıklık süresini de uzatmaktadır (tıkanıklık etkisi nedeniyle).
Talep üzerine otomatik hareketliliğin etkilerinin değerlendirilmesi
temsilci tabanlı simülasyon: Singapur üzerine bir çalışma
Notes: What more can the model give us? Let's see the hourly curves, in this case the travel time index, which is the weighted travel time. The significant increase in veh-km, as expected, results in an increase in network congestion and is reflected in the travel time index, which is plotted in Fig. 14. Not only does the peak hour increase but which prolongs congestion.
What would also be interesting is by using a microscopic model, to examine in more detail the interactions and conflicts between vehicles near intersections, the queues induced by picking up or dropping off a passenger on the sidewalk, etc.
In summary, a key finding is that the unrestricted introduction of AMOD is likely to lead to cannibalization of public transport, which can potentially be mitigated through policies to improve AMOD transport integration, such as discounts for trips terminating at stations. train, prices or limit implementation in certain areas.

## Slide 90
Faaliyete dayalı model, temsilci tabanlı simülasyon ve cep telefonu verilerini birleştirerek kentsel ortamlarda COVID-19 ile ilgili müdahalelerin etkilerini tahmin edilmesi.
Aktivite bazlı modelleme, temsilci tabanlı simülasyon ve cep telefonu verilerini birleştirerek kentsel ortamlarda COVID-19 ile ilgili müdahalelerin etkilerinin tahmin edilmesi.
Notes: Another example of activity-based and Ajan-Tabanlı modelleme is this one, where an epidemiological simulation is built on top of an Ajan-Tabanlı Modelleme.
They can be used to investigate mechanical aspects of infection dynamics over time, such as how they affect certain activities, some closure measures or the consequences of wearing masks in certain situations, school closures...
They used an agent-based MATSim model from Berlin. Our work demonstrates that it is possible to build detailed epidemiological simulations from microscopic mobility models relatively quickly. They built the first prototype in two weeks.
An advantage of using this starting point is that the location of all the simulated people, including the time they spend in a place or on public transport, is already given by the model, which is fed by mobile phone data. Since the input data contains age as an attribute of each synthetic person, it was relatively straightforward to include agent-dependent disease progression in the model from the beginning.
The model includes the effects of different room sizes, air exchange rates, disease importation, changes in activity participation rates over time (from the mobility model, mobility data ), masks, indoor versus outdoor leisure activities, and contact tracing. It has been validated with the dynamics of infection in Berlin (Germany).

## Slide 91
Hastalık ilerleme modeli, her bireyin yaşı veya her bir faaliyette harcanan zaman gibi belirleyici özellikler içerdiğinden Temsilci Tabanlı Modelleme'nin üzerine inşa edilmiştir.
Şekil 3. Hastalık ilerleme modeli. SOL: Durum geçişi [70-75]. SAĞ: Bulaşıcıdan semptomatiğe, semptomatikten ağır hastaya (= hastaneye yatış gerektiren) ve ağır hastadan kritik duruma (= solunum desteği veya yoğun bakım gerektiren) yaşa bağlı geçiş olasılıkları. Kaynak: [15], ikinci sütundaki sayıların 2'ye bölünmesi dışında (Eksik raporlama ve zaman içindeki değişimi bölümünde tartışılmıştır).
Açıkta
Yaş grubu
bulaşıcı vakaların semptomatik duruma gelmesi
hastaneye yatış gerektiren semptomatik vakalar
kritik vakalar gerektiren bir hastane vakasıdır.
bulaşıcı
belirtiler gösteriyor
iyileşti
iyileşti
iyileşti
iyileşti
ağır hasta
ağır hasta
kritik
Faaliyete dayalı model, temsilci tabanlı simülasyon ve cep telefonu verilerini birleştirerek kentsel ortamlarda COVID-19 ile ilgili müdahalelerin etkilerini tahmin edilmesi.

## Slide 92
Her aktivitede, etkileşim süresi, etkileşimin yoğunluğu, mikrobiyal oran göz önüne alındığında enfeksiyon olasılığını modellerler... Temsilci Tabanlı Modelleme, aktivitenin gerçekleştiği yeri verir, ancak kişi başına düşen yüzey alanı, oda boyutları veya diğer temas yoğunluklarının tipik değerleri varsayılmalıdır.
Hem kişi başına düşen alan hem de hava değişim oranı bina kılavuzlarından veya benzer standartlardan alınmıştır; tabloda verilen referanslara dikkat ediniz. Eski binaların/araçların payı bir tahmindir. Üniversitelerin öğrenci başına okullardan iki kat daha fazla alana sahip olduğu varsayılmıştır. Alışveriş, ayak işleri ve ticaretin iş ile aynı özellikleri taşıdığı varsayılmıştır. Temas yoğunlukları eski ve yeni binalar için ayrı ayrı hesaplanmış ve daha sonra eski binaların varsayılan payına göre ortalaması alınmıştır.
Tablo 1. Evdeki temas yoğunluğuna göre normalize edilmiş temas yoğunlukları ci'
Faaliyete dayalı model, temsilci tabanlı simülasyon ve cep telefonu verilerini birleştirerek kentsel ortamlarda COVID-19 ile ilgili müdahalelerin etkilerini tahmin edilmesi.

## Slide 93
Şekil 12. Son model. SOL: yeni vakalar; SAĞ: hastane dolulukları Tüm simülasyon sonuçlarının ortalaması farklı Monte Carlo tohumları ile 10 çalıştırma üzerinden alınmıştır; gölgeli alanlar bu 10 çalıştırmanın %5 ve %95 yüzdelik dilimlerini göstermektedir. Simülasyon modeli yalnızca erken evrede (solda) önemli ölçüde eksik raporlama varsayıldığında hastane sayılarına (sağda) denk düşürülebilir.
Şekil 17. Gerçek verilere kıyasla farklı kalibrasyon çalışmaları için hastaneye yatırılan kişiler. (-) simülasyondaki hastane sayıları, göstergede belirtildiği gibi farklı zaman noktalarına kadar gerçek verilerle (kırmızı noktalar) eşleşecek şekilde kalibre edilmiştir. Bu tarihten sonra örneklem dışı bir tahmin gerçekleştirilir. Kalibrasyon tarihine kadar gerçek hava durumu ve hastalık ithalat verileri kullanılır. Kalibrasyon tarihinden sonra son on yılın ortalama hava durumu verileri kullanılır ve hastalık ithalatı günde 4 ithal vakaya ayarlanır (günde 1 ajan) SOL: Faaliyet seviyeleri kalibrasyon için kullanılan dönemin son gününün seviyesinde dondurulur. SAĞDA: Gerçek faaliyet seviyeleri kullanılır. -Sonuçların ortalaması 30 Monte Carlo tohumu üzerinden alınmıştır.
Faaliyete dayalı model, temsilci tabanlı simülasyon ve cep telefonu verilerini birleştirerek kentsel ortamlarda COVID-19 ile ilgili müdahalelerin etkilerini tahmin edilmesi.

## Slide 94
Model, enfeksiyon sayısının aktivite türüne göre ayrıştırılmasına olanak sağlamaktadır.
Mart Nisan Mayıs Haziran Temmuz Ağustos Eylül Ekim Kasım
2020
yeniden enfeksiyon
Faaliyete dayalı model, temsilci tabanlı simülasyon ve cep telefonu verilerini birleştirerek kentsel ortamlarda COVID-19 ile ilgili müdahalelerin etkilerini tahmin edilmesi.
Notes: More revealing than the number or proportion of infections is the average reproduction number in each type of activity. The method counts for each infected person the number of people they infect in each activity.